## Slide 1
3GPP TSG RAN WG1 Meeting #86 R1-168177 Gothenburg, Sweden, 22nd - 26th Aug 2016
Agenda item: 8.1.5
WF on UL MIMO transmission
Huawei, HiSilicon, China Unicom, Samsung

## Slide 2: Background
In RAN1#85, agreement that the following UL transmission schemes should be studied were achieved
  Non reciprocity based UL MIMO (e.g. PMI based)
  Reciprocity based UL MIMO. E.g. UE derives precoder based on downlink RS measurement (including partial reciprocity)
  Support of MU-MIMO

## Slide 3: Proposal
The following aspects for UL MIMO transmission should be supported:
  Transmission schemes for both reciprocity calibrated UEs, reciprocity non-calibrated UEs, and non-reciprocity case
  Codebook based transmission
    Frequency selective precoding should be considered for large system bandwidth
    E.g., UE–aided and eNB-centric
  Non-codebook based transmission
    E.g., reciprocity based (based on DL RS) transmission only for calibrated UEs
    E.g., UE–aided and eNB-centric: UE recommends candidate UL precoders to eNB based on DL RS measurement , and BS determines the final precoder.