## Slide 1: Way forward on the UL burst duration indication For: Decision AI: 7.2.1.3
Intel, Qualcomm
3GPP TSG-RAN WG1 #86 R1-168178
Gothenburg, Sweden, August 22-26, 2016

## Slide 2: Background
The benefits of signaling the UL burst duration in C-PDCCH is two-fold:
  Power saving: With UL burst duration indication, UE may sleep for the indicated duration, if not scheduled.
  LBT overriding: UL burst duration can be used to override the previous LBT indication in UL grant from Category 4 LBT to single interval LBT.

## Slide 3: Proposal
C-PDCCH indicates a pair of values (UL burst duration, offset)
  UL burst duration is the number of consecutive UL subframes belonging to the same channel occupancy with the DL subframes signaling UL burst duration.
  Offset is the number of subframe to the start of indicated UL burst.
  The LBT procedure for any UL subframe within the signaled UL burst duration for which the eNB had already indicated to perform Category 4 LBT can be switched to an LBT based on 25 us CCA.