## Slide 1
3GPP TSG-RAN1 Meeting #86 R1-168239
Gothenburg, Sweden, 22nd – 26th Aug 2016
WF on evaluation assumptions for initial access in NR
Intel Corporation, […]
Agenda item: 8.1.6

## Slide 2: Link-level evaluation assumptions
 | Below 6GHz | Above 6GHz
Carrier Frequency | 4 GHz | 30, 70 GHz
Channel Model | CDL, AWGN | 
Subcarrier Spacing(s) | 15, 30, 60, 120, 240, or 480 kHz (to be clarified by each proponent; other values are not precluded) | 
SNR range | > -6dB | > -18dB
Search window | The time window to search (correlate) NR-PSS. It depends on the periodicity of NR-SS transmission. The value needs to be provided by each proponent | 
Antenna Configuration at the TRP | (1,1,2) with omni-directional antenna element | (4,8,2), with directional antenna element (HPBW=650, directivity 8dB)
Antenna Configuration at the UE | (1,1,2) with omni-directional antenna element | (2,4,2), with directional antenna element (HPBW=900, directivity 5dB)
Antenna port virtualization | Clarified by each proponent in simulation assumptions (e.g. the beamforming method, beam directions, number of beams) | 
Frequency Offset | Initial acquisition TRP: uniform distribution +/- 0.05 ppm UE: uniform distribution +/- 5, 10, 20 ppm (each company to choose one) Non-initial acquisition TRP: uniform distribution +/- 0.05 ppm UE: uniform distribution +/- 0.1 ppm | 
Number of interfering TRPs | 1. 0 TRP: mandatory 2. 2 interfering TRPs (1st SIR = 0dB, 2nd SIR = -3dB; SIR is defined as the ratio of power between a reference cell and interfered cell) – timing arrival differences from TRPs are provided by each proponent: optional | 1. 0 TRP

## Slide 3: System-level evaluation assumptions
 | Below 6GHz | Above 6GHz
Scenario | Urban Macro (ISD = 500m), Macro only scenario in dense urban (ISD = 200m) | 
Carrier Frequency | 4 GHz | 30, 70 GHz
Channel Model | TR 36.873 | TR 38.900
UE dropping | According to TR 36.873 | 
Subcarrier Spacing(s) | 15, 30, 60, 120, 240, or 480 kHz (to be clarified by each proponent; other values are not precluded) | 
Network Synchronization | TRPs are synchronized, propagation delay difference between TRPs is modelled based on the free space assumption. | 
Search window | The time window to search (correlate) NR-PSS. It depends on the periodicity of NR-SS transmission. The value needs to be provided by each proponent | 
Antenna Configuration at the TRP | (8,1,2) with directional antenna element (HPBW=650, directivity 8dB) | (4,8,2), with directional antenna element (HPBW=650, directivity 8dB)
Antenna Configuration at the UE | (1,1,2) with omni-directional antenna element | (2,4,2), with directional antenna element (HPBW=900, directivity 5dB)
Antenna port virtualization | Clarified by each proponent in simulation assumptions (e.g. the beamforming method, beam directions, number of beams) | 
Frequency Offset | Initial acquisition TRP: uniform distribution +/- 0.05 ppm UE: uniform distribution +/- 5, 10, 20 ppm (each company to choose one) Non-initial acquisition TRP: uniform distribution +/- 0.05 ppm UE: uniform distribution +/- 0.1 ppm | 
PHY Abstraction | No PHY Abstraction. All the links shall be explicitly implemented in the system level platform. | 

## Slide 4: Performance metrics
Signal detection rate
Misdetection probability
Distribution of acquisition time (a.k.a. cell search time)
Residual timing and frequency errors after synchronization
Other metrics (e.g., PAPR) are not precluded
Note: Proponents should specify the target false alarm probability
Note: Proponents should open detailed synchronization signal designs including synchronization signal bandwidth
Note: It is recommended to assume the same amount of information
Note: Search duty cycle is 100% (i.e. receiver is always ON)