## Slide 1: WF on Frame Structure
Ericsson, Huawei, Qualcomm, Nokia, Sony, DoCoMo, MediaTek, Fujitsu, CATT, Intel, ZTE, InterDigital
R1-168294
8.1.3.2

## Slide 2: Proposal
Subframe
  Already agreed upon
  Assume x=14 in the reference numerology for subframe definition (for normal CP)
  FFS: y=x and/or y=x/2
Slot
  Slot of duration y OFDM symbols in the numerology used for transmission
  An integer number of slots fit within one subframe duration (at least for transmission numerologies shorter than or equal the reference numerology)
  The structure allows for ctrl at the beginning
  The structure allows for ctrl at the end
  The structure allows for ctrl at the end and at the beginning
  One possible scheduling unit
Mini-slot
  Should at least support transmission shorter than y OFDM symbols in the numerology used for transmission
  May contain ctrl at the beginning and/or ctrl at the end
  The smallest mini-slot is the smallest possible scheduling unit (FFS: smallest number of symbols)
Note: the names are for the purpose of discussion. Whether some terms can be merged or not is FFS