## Slide 1: Way forward on prioritizing of SL V2V transmission
NTT DOCOMO, CMCC
R1-168302
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden 22nd - 26th August 2016 Agenda item 7.2.2.6

## Slide 2: Background
In RAN1#84bis, the following agreement on coexistence of PC5-based V2V operation and legacy Uu operation is made:
The followings are supported for the purpose of coexistence between PC5-based V2V and WAN:
  Sidelink open loop power control is re-used for SL TX for V2V
    FFS RSRP based resource selection
  SL TX for V2V can be prioritized over WAN TX
    FFS the details (e.g., applicability to Mode 1 and/or Mode 2, etc.), especially whether existing D2D mechanism can be reused,
    The prioritization is managable by eNB. Details FFS.
  The same receiver capability of D2D communication UEs is assumed for V2V UEs. That is, a Rx chain is available at all time to receive V2V signals without affecting WAN reception (from RAN1 perspective) when the UE is configured to receive V2V.

## Slide 3: Proposal
UE prioritizes WAN UL Tx over SL V2V Tx with following exception(s).
  Rel-13 SL TX gap is extended for prioritization of SL V2V Tx over WAN UL Tx.
    Gap pattern needs to be optimized to cover SL V2V Tx.
      Details are up to RAN2.
  UE can only prioritize SL V2V Tx over WAN UL Tx during configured Tx gap.