## Slide 1: Way Forward MUST power ratios
Huawei, HiSilicon, Media Tek
3GPP TSG RAN WG1 Meeting #86 R1-168316
Gothenburg, Sweden 22nd - 26th August 2016
Agenda item 7.2.5.1

## Slide 2: Background
In RAN1#85 some agreements were achieved
Agreement:
For Case 1 and 2, and for each combination of modulation order,
  The number of power ratios generating non-uniform composite constellation should be chosen from 0 (for some combinations, if any), 1, 2 or 3.
    The details are FFS.
  Power ratios generating non-uniform composite constellation should be selected from the range [0.7, 0.95].
    The values of power ratio is FFS.
    0.7 should be excluded in case of 64QAM (for near UE) + QPSK (for far UE).

## Slide 3: Background
Different power ratio values are proposed by different companies for QPSK+QPSK. Performance is one aspects, but we’d better set some guidelines for the power ratios generation so that the power ratios could be converged.
Some proposed power ratio values from different companies |  |  |  |  | 
Candidate index | 1 | 2 | 3 | 4 | 5
HW | 0.7353 | 0.8000 | 0.9000 | 0.9412 | 
Qualcomm | 9/13=0.692 | 4/5=0.8 | 25/29=0.862 | 16/17=0.941 | 36/37=0.973
NOKIA | 9/13=0.692 | 0.8 | 0.862 | 0.941 | 
LG | TBD | TBD | 0.9 | TBD | 
NTT DOCOMO | 0.77 | 0.8 | 0.83 | 0.86 | 
ZTE | 0.75 | 0.8 | 0.9 | 0.95 | 

## Slide 4: Background
The power ratios can be generated using the grid coordinates which can make the UE implementation with lower complexity compared with other power ratio values.
The generated power ratios using grid coordinates will not affect the performance as long as the generated power ratios are close enough to the optimum power ratios.

## Slide 5: Background
Grid coordinates of the right figure to generate the power ratios for different modulation combinations.
Grid coordinates points
n
k

## Slide 6: Proposals
Use the grid coordinates to generate the power ratios for MUST case 1&2 for different modulation combinations.
FFS: specific power ratio values

## Slide 7: Appendix
For QPSK+QPSK
k\n | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
1 | 0.9000 | 0.9615 | … |  |  |  |  |  |  |  |  |  |  | 
2 | 0.8000 | 0.9000 | 0.9412 | 0.9615 | … |  |  |  |  |  |  |  |  | 
3 | 0.7353 | 0.8448 | 0.9000 | 0.9308 | 0.9494 | 0.9615 | … |  |  |  |  |  |  | 
4 | 0.6923 | 0.8000 | 0.8621 | 0.9000 | 0.9245 | 0.9412 | 0.9529 | 0.9615 | … |  |  |  |  | 
5 | 0.6622 | 0.7642 | 0.8288 | 0.8711 | 0.9000 | 0.9204 | 0.9352 | 0.9464 | 0.9549 | 0.9615 |  |  |  | 
6 | 0.6400 | 0.7353 | 0.8000 | 0.8448 | 0.8767 | 0.9000 | 0.9174 | 0.9308 | 0.9412 |  |  |  |  | 
7 | 0.6231 | 0.7118 | 0.7752 | 0.8212 | 0.8550 | 0.8805 | 0.9000 | 0.9152 |  |  |  |  |  | 
8 | 0.6098 | 0.6923 | 0.7538 | 0.8000 | 0.8351 | 0.8621 | 0.8832 |  |  |  |  |  |  | 
9 | 0.5990 | 0.6760 | 0.7353 | 0.7811 | 0.8167 | 0.8448 |  |  |  |  |  |  |  | 
10 | 0.5902 | 0.6622 | 0.7191 | 0.7642 | 0.8000 |  |  |  |  |  |  |  |  | 
11 | 0.5828 | 0.6503 | 0.7049 | 0.7490 |  |  |  |  |  |  |  |  |  | 
12 | 0.5765 | 0.6400 | 0.6923 |  |  |  |  |  |  |  |  |  |  | 
13 | 0.5711 | 0.6310 |  |  |  |  |  |  |  |  |  |  |  | 
14 | 0.5664 |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 8: Appendix
QPSK+16QAM
k\n | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
1 | 0.8333 | 0.9074 | 0.9419 | 0.9603 | … |  |  |  |  |  |  |  |  | 
2 | 0.7619 | 0.8333 | 0.8780 | 0.9074 | 0.9275 | 0.9419 | 0.9524 | 0.9603 | … |  |  |  |  | 
3 | 0.7289 | 0.7897 | 0.8333 | 0.8653 | 0.8892 | 0.9074 | … |  |  |  |  |  |  | 
4 | 0.7101 | 0.7619 | 0.8020 |  |  |  |  |  |  |  |  |  |  | 
QPSK+64QAM
k\n | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
1 | 0.7941 | 0.8521 | 0.8895 | 0.9146 | 0.9323 | 0.9450 | 0.9545 | 0.9618 |  |  |  |  |  | 
2 | 0.7529 |  |  |  |  |  |  |  |  |  |  |  |  |