## Slide 1: Way forward on Cyclic Prefix
Huawei, HiSilicon, LGE, Sony, Vodafone, Intel, CATR, CMCC Ericsson, Orange, Mediatek, Verizon, InterDigital, OPPO, CATT, China Telecom, AT&T
3GPP TSG RAN WG1 #86
Gothenburg, Sweden August 22-26, 2016
Agenda item:8.1.3.1
Document for decision
R1-168321

## Slide 2: Observation
In [1][2][3][4][5], for the evaluated scenarios extended CP show benefits.
  [1] R1-166100, Huawei, Hisilicon
  [2] R1-166652, Sony
  [3] R1-166879, LGE
  [4] R1-167107, CMCC
  [5] R1-167108, CMCC

## Slide 3: Proposals
More than one CP length should be supported for a given sub-carrier spacing
  The different CP lengths for a given sub-carrier spacing should be of substantially different lengths.
  For 60 kHz subcarrier spacing, at least one CP length is similar to the normal CP length of 15 kHz corresponding to LTE numerology
Note: FFS whether all of sub-carrier spacings support more than one CP length or not
Note: FFS whether supporting more than one CP length for a given sub-carrier spacing is mandatory or optional for a given UE