## Slide 1: WF on observations on performance aspects of NB-IoT positioning
Huawei, HiSilicon, iTL …
R1-168332
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, August 22-26, 2016
Agenda item 7.2.11.1.4

## Slide 2: Background
The Rel-14 NB-IoT enhancements WID asks RAN1 to study both UTDOA and OTDOA for NB-IoT, and to provide recommendation to RAN#73 as the basis to make a choice
A way forward for reporting to RAN#73 was agreed in RAN1#86 and the observations on the following aspects regarding performance should be reported:
  Report the horizontal accuracy and TOA estimation accuracy at 67%.
  Report observations on time to determine position according to MCL
    This is the time from trigger for positioning to availability of a positioning estimate
  Report observations on impact of having a lower power class UE
  Report dependency of accuracy performance on synchronous (E-SMLC is assumed to know the absolute timing of each involved eNB ) or asynchronous networks
  Requirements are the same for all three operation modes (i.e. stand-alone/in-band/guard band) per the WID

## Slide 3: Observations
Horizontal accuracy of UTDOA
  For NB-IoT UEs with transmit power of 23 dBm, the positioning accuracy of UTDOA schemes evaluated for RAN1#86 varies from 21 m to 133 m at 67% with EPA1 channel and from 129 m to 227 m at 67% with ETU1 channel.
    The evaluations are all based on synchronous network
  The accuracy of UTDOA is common for in-band, guard-band, and standalone operations.
  The accuracy of UTDOA may degrade with the new lower power class(es) for NB-IoT UE.
  (this sentence is not staying here) Companies have used differing simulation assumptions, which leads to the performance differences between companies. Comparisons can be made within each company’s results
Company | Accuracy (m @ 67%) indoor UEs |  | UE Tx power (dBm) | Positioning signal
 | EPA1 | ETU1 |  | 
Ericsson | 81~133 | 129~227 | 23 | NPRACH with 32 repetitions
Huawei | 21~46 |  |  | NPRACH-like positioning signal with 180 kHz hopping bandwidth and 128 repetitions
ZTE | 150~250 |  |  | NPRACH hopping within 1 PRB or 6 PRBs with 32 repetitions or 128 repetitions
NOTE: Company names will be anonymized for reporting to RAN

## Slide 4: Observations
TOA estimation accuracy in UTDOA
MCL | Company | TOA estimation error | Channel model | Positioning signal
164dB | HUAWEI | [-0.13us, 0.13us] @ 90% | EPA 1 | NPRACH-like positioning signal with 180 kHz hopping bandwidth and 128 repetitions
 |  | [-0.585us, 0.585us] @ 90% | EPA 1 | NPRACH with 128 repetitions
 | QUALCOMM | [-1, 2]us @ 90% | ETU1 | NPRACH with 128 repetitions
 |  | [-1.3, 1.3]us @ 90% | AWGN | NPRACH with 128 repetitions
154dB | HUAWEI | [-0.065us, 0.065us] @ 93.60% | EPA 1 | NPRACH-like positioning signal with 180 kHz hopping bandwidth and 128 repetitions
 |  | [-0.26us, 0.26us] @ 90% | EPA 1 | NPRACH with 128 repetitions
 | QUALCOMM | [0.3, 0.8]us @ 90% | ETU1 | NPRACH with 256 repetitions
 |  | [-0.25, 0.25]us @ 90% | AWGN | NPRACH with 256 repetitions
 | Fraunhofer IIS | < 2.6us @90% | TU | New uplink positioning signal in 100 subframes
 |  | < 0.6us @90% | RA | 
144dB | HUAWEI | [-0.065us, 0.065us] @ 95.50% | EPA 1 | NPRACH-like positioning signal with 180 kHz hopping bandwidth and 128 repetitions
 |  | [-0.26us, 0.26us] @ 90% | EPA 1 | NPRACH with 128 repetitions
 | QUALCOMM | [-0.1, 1.2]us @ 90% | ETU1 | NPRACH with 16 repetitions
 |  | [-0.25, 0.25]us @ 90% | AWGN | NPRACH with 16 repetitions
NOTE: Company names will be anonymized for reporting to RAN

## Slide 5: Observations
Horizontal accuracy of OTDOA
  For in-band operation, the positioning accuracy of OTDOA schemes evaluated by RAN1#86 reported by most companies is on the order of tens of meters. One evaluation found accuracy on the order of a few hundred meters
    The evaluations are all based on synchronous network (E-SMLC is assumed to know the absolute timing of each involved eNB)
  For standalone operation, the positioning accuracy of OTDOA was reported by one company as on the order of tens of meters.
  The accuracy of OTDOA does not depend on UE power class.
Company | Accuracy (m @ 67%) indoor UEs |  | eNB Tx power (dBm) | Positioning signal | Sampling rate (kHz)
 | EPA1 | ETU1 |  |  | 
Ericsson | 326~427 | 326~427 | 43 dBm for standalone, 35 dBm for in-band | Reusing NPSS | 240
Huawei | 45 for in-band 26 for standalone |  |  | Reusing NSSS | 15360
Nokia | 7~11 | 40~135 |  | New PRS with 180 kHz ~ 10 MHz hopping bandwidth | 
ZTE | 31~52 |  |  | New PRS with multi-PRB hopping | 1920
NOTE: Company names will be anonymized for reporting to RAN

## Slide 6: Observations
TOA estimation accuracy in OTDOA
Deployment mode | MCL | Company | TOA estimation error | Channel model | Positioning signal
Inband/guard band | 164dB | HUAWEI | [-0.195us, 0.195us] @ 90% | EPA 1 | NSSS(2400 ms)
 |  | QUALCOMM | [0.3, 0.7]us @ 90% | ETU1 | NPRS-based(6963ms)
 |  |  | [-0.09, 0.11]us @ 90% | AWGN | NPRS-based(6963ms)
 | 154dB | HUAWEI | [-0.065us, 0.065us] @ 98.40% | EPA 1 | NSSS(2400 ms)
 |  | QUALCOMM | [0, 1.3]us @ 90% | ETU1 | NPRS-based(1741ms)
 |  |  | [-0.04, 0.06]us @ 90% | AWGN | NPRS-based(1741ms)
 |  | Fraunhofer IIS | < 2.6 us @ 90% | TU | NPRS-based(1ms)
 |  |  | < 0.27 us @ 90% | RA | NPRS-based(1ms)
 | 144dB | HUAWEI | [-0.065us, 0.065us] @ 100% | EPA 1 | NSSS(2400 ms)
 |  | QUALCOMM | [-0.5, 1.6]us @ 90% | ETU1 | NPRS-based(112ms)
 |  |  | [-0.04, 0.06]us @ 90% | AWGN | NPRS-based(112ms)
Standalone | 164dB | HUAWEI | [-0.065us, 0.065us] @ 98.30% | EPA 1 | NSSS(2400 ms)
 | 154dB | HUAWEI | [-0.065us, 0.065us] @ 100% | EPA 1 | NSSS(2400 ms)
 | 144dB | HUAWEI | [-0.065us, 0.065us] @ 100% | EPA 1 | NSSS(2400 ms)
NOTE: Company names will be anonymized for reporting to RAN