## Slide 1: WF on observations on network impact aspects of NB-IoT positioning
Huawei, HiSilicon, …
R1-168334
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, August 22-26, 2016
Agenda item 7.2.11.1.4

## Slide 2: Background
The Rel-14 NB-IoT enhancements WID asks RAN1 to study both UTDOA and OTDOA for NB-IoT, and to provide recommendation to RAN#73 as the basis to make a choice
A way forward for reporting to RAN#73 was agreed in RAN1#86 and the observations on the following aspects regarding network impact should be reported:
  Report observations on network complexity/cost, for example including LMUs (as described in 36.111)
  Report scalability to support massive numbers of UEs per cell
  Report dependency of accuracy performance on synchronous (E-SMLC is assumed to know the absolute timing of each involved eNB ) or asynchronous networks

## Slide 3: Observations
Impact to network complexity/cost
  Enhanced Serving Mobile Location Center (E-SMLC) and MME to E-SMLC signaling links are needed for both UTDOA and OTDOA.
  For UTDOA, Location Measurement Unit (LMU), and LMU to E-SMLC signaling links are needed to implement measurement for positioning.
    Note there are 3 different types of LMU defined in 36.111, including ‘Class 1: Integrated into basestation’
  Both OTDOA and UTDOA can work with both synchronous and asynchronous network
Scalability to support massive numbers of UEs per cells
  For UTDOA, the uplink time-frequency resources required in the serving cell for transmitting uplink positioning signal increases with increased cell positioning load.
  For UTDOA, the basestation processing load (e.g., uplink measurements) increases with increased positioning load.
  For UTDOA the UL positioning resources are coordinated across a set of cells
  For OTDOA, the uplink time-frequency resources required for reporting measurements increases with increased positioning load.
  For OTDOA, the downlink time-frequency resources for transmitting downlink positioning reference signal depend on system configuration rather than number of UEs
  For OTDOA, the basestation processing load may not increase with increased positioning load.