## Slide 1: WF on time-domain structure in NR (update from R1-168167?)
Panasonic, [LG Electronics],,
3GPP TSG RAN WG1 Meeting #86 R1-168341
Gothenburg, Sweden, 22nd - 26th Aug 2016
Agenda Item: 8.1.3.2

## Slide 2: Discussion
Unpaired band operation of DL to UL switching requires at least one symbol overhead. Smaller overhead is better from the efficiency point.
More switching means to reduce the latency of unpaired band operation. More often is better from latency perspective. Considering 0.5ms URLLC latency requirement, roughly once less than 0.125ms is useful. Note that paired band latency is only limited by TTI length only.
I propose following.
  15kHz Subcarrier spacing Normal CP: Y=14. This is for the alignment with special subframe and efficiency purpose.
  30kHz subcarrier spacing and higher of Normal CP: Y roughly corresponds to 0.125ms.
How often DL/UL switching? | Min overhead consumed by gap | Duration in case of 15 kHz SC | Duration in case of 30 kHz SC | Duration in case of 60 kHz SC | Duration in case of 120 kHz SC | Duration in case of 240 kHz SC
every 3 symbols | 33% | 0.214ms | 0.107ms | 0.054ms | 0.026ms | 0.013ms
every 4 symbols | 25% | 0.29ms | 0.143ms | 0.071ms | 0.036ms | 0.017ms
every 7 symbols | 14% | 0.5ms | 0.25ms | 0.125ms | 0.063ms | 0.032ms
every 14 symbols | 7% | 1ms | 0.5ms | 0.25ms | 0.125ms | 0.063ms

## Slide 3: Proposal
In case of the same numerology between DL and UL, within a time duration of y OFDM symbols, the following are supported
  DL portion
    DL portion size can be from 0 to y symbol time duration from the start of the time duration
    At least 0, y, one value within the range (0,y) are supported
    Within a DL portion, one or multiple mini slots can be available.
  UL portion
    UL portion size can be from 0 to y symbol time duration
    At least 0, y, one value within the range (0,y) are supported
    The time-location of UL portion within a time transmission duration can be flexible
    Within a UL portion, one or multiple mini slots can be available.
  Each of DL portion and UL portion is contiguous.
  The spec should allow DL portion and UL portion is TDMed with a gap (in case of non-full duplex)
At least following is supported.
  y = 14 in 15 kHz subcarrier spacing in normal CP
  FFS: y= 7 with 15 kHz subcarrier spacing in normal CP
FFS: The time duration y is the same as the subframe duration and/or a multiple of the time durations present in the subframe duration.
FFS: different numerology between DL and UL
FFS: time duration of y starts from UL
FFS: whether and how to extend the discussion on DL portion/UL portion length required for the coexistence with LTE TDD.

## Slide 4: background
Agreement on Monday in this meeting on the subframe
Agreements:
A subframe duration is defined by the duration of x OFDM symbols given a reference numerology
  With the same CP overhead, a single value of x is specified irrespective of the subcarrier spacing value chosen for the reference numerology
  This does not preclude multiple data transmission opportunities in time within a subframe duration
  This does not preclude multiple control transmission opportunities in time for both DL and UL within the subframe duration
  This does not preclude one data transmission to span over multiple subframe durations
A UE has one reference numerology in a given NR carrier which defines subframe duration for the given NR carrier
  FFS: In a given NR carrier, whether different UEs may have different reference numerologies or may not
Specification supports multiplexing numerologies in TDM and/or FDM within/across (a) subframe duration(s) from a UE perspective

## Slide 5: background
Agreement on time interval X in the last meeting:
Agreements:
At least the following should be supported for NR in a frequency portion
  A time interval X which can contain one or more of the following
    DL transmission part
    Guard
    UL transmission part
  FFS which combinations are supported and whether they are indicated dynamically and/or semi-statically
  Furthermore, the following is supported
    The DL transmission part of time interval X to contain downlink control information and/or downlink data transmissions and/or reference signals
    The UL transmission part of time interval X to contain uplink control information and/or uplink data transmissions and/or reference signals
  FFS length(s) of time interval X
  FFS: other characteristics of time interval X
  Note: The usage of DL and UL does not preclude other deployment scenarios e.g., sidelink, backhaul, relay