## Slide 1
WF on additional RS for NR
LG Electronics, Samsung, NTT DOCOMO
R1-168347
3GPP TSG RAN1 #86
Gothenburg, Sweden 22-26 Aug 2016
Agenda Item: 8.1.3.2

## Slide 2: Background (1/2)
Agreement in RAN#85,
  At least the following is studied for NR in order to reduce decoding latency
    RS used to start to demodulate a data transmission is located at the beginning of the time interval to which the data and associated RS for demodulation is physically mapped

## Slide 3: Background (2/2)
For NR system design, various requirements are considered as follows:
  Frequency bands: 700MHz, 2GHz, 4GHz, 30GHz, 70GHz
  Velocity: up to 500km/h
  Environments: Indoor, Dense urban, High speed, Urban macro, Extremely large coverage
  Service Types: eMBB, URLLC, mMTC
Since requirements for NR are diverged, it seems hard to meet all requirements using single RS structure.

## Slide 4: Proposal
In addition to the front-loaded RS component agreed to study in RAN1#85, additional RS component(s) is/are studied for data demodulation in NR for supporting estimation of the following:
  Doppler parameters (e.g. Doppler spread, Doppler shift)
  Phase rotation and frequency offset
  Note: these RS components may be defined with the same or different antenna ports