## Slide 1: Way forward on sPDCCH
Huawei, HiSilicon,Qualcomm,Ericsson,Nokia,ASB,InterDigital,Xiaomi Communication, NTT DOCOMO,CATT, Samsung,Intel,LG,ZTE, ZTE Microelectronics, Spreadtrum,Sharp,CATR,Panasonic,Potevio, Mediatek, Motorola Mobility, Lenovo, NEC,SONY
3GPP TSG RAN WG1 #86 R1-168350
Gothenburg, Sweden 22nd - 26th August 2016
Agenda item: 7.2.12.2.1

## Slide 2: Proposals
Legacy PDCCH can be used to transmit sDCI (DCI for sPDSCH and/or sPUSCH) .
QPSK is used for sPDCCH.
Tail biting convolutional coding is used for sPDCCH.
For CRS-based sPDCCH,
  In time domain,
    sPDCCH is transmitted from the first OFDM symbol within an sTTI
      sPDCCH is not mapped to the PDCCH region.
      FFS number of OFDM symbols of the sPDCCH
  Frequency resource for sPDCCH can be informed by eNB.