## Slide 1: WF on Modeling Line-of-Sight Blockage for V2V
Huawei, HiSilicon, Volkswagen, Ericsson, General Motors, Vodafone, [Fraunhofer HHI], [LGE]
3GPP TSG RAN WG1 Meeting #86 R1-168370
Gothenburg, Sweden, 22nd - 26th August 2016
Agenda item: 8.1.7

## Slide 2: Background
Realistic LOS blockage modeling is particularly important for V2V communication because of:
  safety-critical characteristics of many applications
  low antenna heights
Other vehicles often block V2V communication
  Same applies to other V2X link types (e.g., V2P)
3GPP UMi LOS model (used for V2V LOS) generates unrealistically large number of transitions between propagation states (shown in [4])
Up to 40% of links blocked by vehicles in urban

## Slide 3: Relationship to Ch. Coeff. Generation Process [1]
12-step channel coefficient generation process adopted by WINNER models and TR38.900 [1]
  Improves 2nd step of process for V2V

## Slide 4: Proposal 1: introduce new propagation state for V2V
Model the propagation condition of V2V links using three states:
  i) LOS
  ii) non-LOS (NLOS) due to static objects (buildings, trees)*
  iii) NLOS due to mobile objects (vehicles)*
I.e., not only distinguishing LOS and NLOS, but further dividing NLOS into NLOS due to static and NLOS due to mobile objects
* It was shown in previous studies [2],[3] that these two states result in considerably different channels

## Slide 5: Proposal 2: Model V2V LOS Blockage Evolution
Model evolution of V2V LOS blockage
  Ensure transition between three states (LOS, NLOS due to static objects, NLOS due to mobile objects) in consistent manner
  E.g., abstracted from real maps of cities and highways and real vehicular mobility
One example of a simple model: Markov chain (3 states: LOS, NLOSv, NLOSb)
  I.e., use a computationally simple model for assigning consistent propagation states for V2V

## Slide 6: References
[1] 3GPP TR 38.900, “Channel model for frequency spectrum above 6 GHz”, v2.0.0, June 2016.
[2] T. Abbas, K. Sjöberg, J. Karedal, and F. Tufvesson, “A measurement based shadow fading model for vehicle-to-vehicle network simulations,” International Journal of Antennas and Propagation, 2015.
[3] M. Boban, J. Barros, and O. Tonguz, “Geometry-based vehicle-to-vehicle channel modeling for large-scale simulation,” IEEE Transactions on Vehicular Technology, Vol. 63, No. 9, November 2014.
[4] R1-167219, Modeling the Evolution of Line-of-Sight Blockage for V2V Channels, 3GPP TSG-RAN1 Meeting #86, Gothenburg, Aug. 2016.