## Slide 1: WF on channel model issues for flexible duplex evaluation
Huawei, HiSilicon, Intel
3GPP TSG RAN1 #86
Gothenburg, Sweden, Aug 22 - 26, 2016
Agenda Item: 8.1.7
R1-168372

## Slide 2
Parameters | Dense urban | Urban macro | Indoor hotspot
Fast fading parameters | Below 6GHz: Macro-to-UE: 3D UMa Micro-to-UE: 3D Umi Macro to Macro: 3D UMa O-to-O (h_UE=25m); ASA and ZSA statistics* updated to be the same as ASD and ZSD; ZoD offset = 0 Macro to Micro: 3D Uma O-to-O Micro to Micro: 3D Umi O-to-O (h_UE=10m); ASA and ZSA statistics updated to be the same as ASD and ZSD; ZoD offset = 0 UE to UE: InH for indoor to indoor, and 3D Umi for other cases. ASD and ZSD statistics updated to be the same as ASA and ZSA. Dual mobility support. Above 6GHz: Macro-to-UE: 5GCM UMa Micro-to-UE: 5GCM Umi Macro to macro: 5GCM UMa O-to-O (h_UE=25m); ASA and ZSA statistics updated to be the same as ASD and ZSD; ZoD offset = 0 Macro to micro: 5GCM UMa O-to-O Micro to Micro: 5GCM UMi O-to-O (h_UE=10m); ASA and ZSA statistics updated to be the same as ASD and ZSD; ZoD offset = 0 UE to UE: 5GCM UMi; ASD and ZSD statistics updated to be the same as ASA and ZSA. Dual mobility support. |  | Below 6GHz: TRP-to-UE: ITU InH TRP-to-TRP: ITU InH (h_UE=3m), ASA statistics updated to be the same as ASD UE-to-UE: A.2.1.2 in TR36.843 (ITU InH), ASD statistics updated to be the same as ASA. Above 6GHz: TRP-to-UE: 5GCM Indoor-office TRP-to-TRP: 5GCM Indoor-office (h_UE=3m), ASA and ZSA statistics* updated to be the same as ASD and ZSD UE-to-UE: 5GCM Indoor-office (h_BS=1.5m), ASD and ZSD statistics updated to be the same as ASA and ZSA
Proposal
* NOTE: Statistics of ASA/ASD and ZSA/ZSD include its mean, standard variance, correlation distance in the horizontal plane, and in-cluster angular spread (e.g., cluster ASA/ASD)
The following assumption is used as starting point for flexible duplex evaluation, and further update might be made after more measurements are available.