## Slide 1: WF on V2V priority specific thresholds
Intel
3GPP TSG RAN WG1 Meeting #86 R1-168380
Gothenburg, Sweden, 22nd - 26th August 2016
Agenda item - 7.2.2.2.1

## Slide 2: Background
The following working assumption was made at the RAN1# 85 meeting:
  SCI explicitly includes priority information.
    FFS how this priority information is exactly transmitted in SCI
    Priority information in a decoded SCI is used in resource (re)selection
    Priority information in a decoded SCI is not used as a condition to trigger resource reselection
    Priority information in a decoded SCI is not used as a condition to drop transmission

## Slide 3: Background
Resource reselection procedure depends on
  Priority information of UEs sharing resources
  Priority of the UE performing resource reselection
Example of priority configuration settings
 |  | Priority of other UEs sharing spectrum resources (Thr3≤ Thr2≤ Thr1≤ Thr0) |  |  | 
 |  | Priority 0 (Lowest) | Priority 1 | Priority 2 | Priority 3 (Highest)
UE reselecting resource | Priority 0 | Threshold 0 | Threshold 1 | Threshold 2 | Threshold 3
 | Priority 1 | Threshold 1 | Threshold 1 | Threshold 2 | Threshold 3
 | Priority 2 | Threshold 2 | Threshold 2 | Threshold 2 | Threshold 3
 | Priority 3 | Threshold 3 | Threshold 3 | Threshold 3 | Threshold 3

## Slide 4: Proposal
  Step#2 of resource reselection procedure
  Priority specific RSRP thresholds are configured for step#2 of resource reselection procedure (exclusion of resources)
  Set of priority specific RSRP thresholds is configured independently for each transmission priority level of UE performing reselection
  Step #3 of resource reselection procedure is priority independent