## Slide 1: WF on UL LLS for MA
Huawei, HiSilicon, CATR, CATT, Spreadtrum, Fujitsu, CMCC, InterDigital, China Telecom,
[Samsung], [ZTE], [Intel], [LGE], [Orange], [Vodafone], [Qualcomm], […]
3GPP TSG RAN WG1 #86 R1-16xxxx
Gothenburg, Sweden, Aug. 22-26, 2016
Agenda item: 8.1.2.2

## Slide 2: Observations
The following non-orthogonal multiple access schemes have been reported up to RAN1#86 for at least UL NR MA (listed in the order of proposed time, i.e., increasing tdoc number)
  Sparse code multiple access (SCMA) (e.g., R1-162153)
  Multi-user shared access (MUSA) (e.g., R1-162226)
  Low code rate spreading (e.g., R1-162385)
  Frequency domain spreading (e.g., R1-162385)
  Non-orthogonal coded multiple access (NCMA) (e.g., R1-162517)
  Non-orthogonal multiple access (NOMA) (e.g., R1-163111)
  Pattern division multiple access (PDMA) (e.g., R1-163383)
  Resource spread multiple access (RSMA) (e.g., R1-163510)
  Interleave-Grid Multiple Access (IGMA), (e.g., R1-163992)
  Low density spreading with signature vector extension (LDS-SVE) (e.g., R1-164329)
  Low code rate and signature based shared access (LSSA), (e.g., R1-164869)
  Non-orthogonal coded access (NOCA), (e.g., R1-165019)
  Interleave Division Multiple Access (IDMA), (e.g., R1-165021)
  Repetition division multiple access (RDMA), (e.g., R1-167535)
  Group Orthogonal Coded Access (GOCA), (e.g., R1-167535)

## Slide 3: Table 1
Further specified values reported w.r.t. agreed parameter table in RAN1#84bis
Parameters | Values or assumptions | Further specified values reported
Carrier Frequency | 2 GHz | 
Waveform | OFDM /SC-FDMA Other waveform is not precluded | OFDMA with equal bandwidth and distributed subcarrier allocation or OFDMA with orthogonal Walsh code
Numerology | Same as Release 13 | 
System Bandwidth | 10 MHz | Allocated bandwidth reported: 4RB, 6RB, 12RB The same for non-orthogonal MA and OFDMA
Target spectral efficiency | Proponents report per UE spectral efficiency and the number of UEs multiplexed if multi-UEs LLS is assumed | The same target per UE spectral efficiency for non-orthogonal MA and OFDMA Without short-term (per TTI) MCS adaptation Detail of reported target SE per user and the number of users are listed in Table 3
BS antenna configuration | 2/4 Rx as baseline 8Rx optional | See Table 3
UE antenna configuration | 1Tx | 
Transmission mode | TM1 (refer to TS36.213) | 
SNR distribution of Multiple UEs | Proponents report if single-user or multi-user LLS is used, and what SNR distribution is assumed. | Either equal long-term SNR and/or unequal long-term SNR has been considered Detail of assumptions listed in Table 3
Propagation channel & UE velocity | TDL for in TR38.900 as mandatory EPA, EVA, ETU as optional 3km/h, 30km/h, 120km/h | See Table 3
Max number of HARQ transmission | 1, 4 | 1

## Slide 4: Table 2
Further assumptions for UL LLS
Parameters | Specified assumptions reported
Channel estimation | Either ideal and/or realistic channel estimation has been considered Detail of assumptions listed in Table 3
MA signature allocation | Either fixed and/or random MA signature (e.g., codebook, sequence, interleaver, etc.) allocation has been considered Detail of assumptions listed in Table 3
Timing/frequency offset | Frequency offset not considered Timing offset of either within CP and/or beyond CP has been considered Detail of assumptions listed in Table 3
SNR definition | SNR is either defined at the transmitter per layer or at the receiver as the sum per RE

## Slide 5: Table 3
 | SCMA | MUSA | PDMA | LDS-SVE | IGMA | NCMA | NOCA | LSSA | NOMA
Contributions | R1-164037 R1-166094 R1-167105 R1-165435 R1-167602 | R1-166404 | R1-165287 R1-167870 R1-165435 R1-167602 | R1-164329 R1-166670 | R1-166750 | R1-164557 R1-166876 | R1-165019 R1-167249 | R1-167340 | R1-167537
Spectral efficiency (bps/Hz per UE) | 0.05~0.5 | 0.125 | 0.25, 0.375 | 0.25, 0.375 | 0.1~0.72 | 0.25 | 1/12 | 0.0833, 0.125, 0.166, 0.25, 0.375 | 0.25, 0.5
Number of UEs | 4, 6, 8, 12 | 4, 6, 8, 12, 16 | 4, 8, 12 | 6 | 6 (8~16 not compared with OFDMA) | 3~7(SF=4) 3~6(SF=2) | 12, 18, 24 | 4, 6, 8, 12, 24 | 2
Channel Type | TDL-A, TDL-C, EPA | TDL-C | TDL-A, TDL-C, EPA | TDL-A, TDL-B, TDL-C | TDL-A, TDL-C, | TDL-C | ETU | TDL-C | TDL-C
Antenna Config. | 1T2R 1T4R | 1T2R | 1T2R | 1T2R | 1T2R | 1T2R | 1T2R | 1T2R | 1T2R
SNR distribution | Equal/ unequal | Equal/ unequal | Equal | Equal | Equal | Equal | Equal/ unequal | Equal | Equal/ unequal
MA signature allocation | Fixed/ random | Random | Fixed | Fixed | Fixed/ random | Fixed | Fixed | Fixed | Fixed
Channel estimation | Ideal | Ideal | Ideal | Ideal | Ideal/ realistic | Ideal/ realistic | Ideal | Ideal | Ideal/ realistic
Timing offset | Within CP | Within CP | Within CP | Within CP | Within CP | Within CP | Within CP/ beyond CP | Within CP | Within CP
Table of contributions comparing non-orthogonal MA schemes with OFDMA

## Slide 6: Observations
It is observed that non-orthogonal MA outperforms OFDMA in terms of UL link-level sum throughput [1] and overloading capability in the evaluated scenarios
[1] R1-163560, Way forward on assumptions for multiple access evaluation, RAN1#84b, Busan, Korea.

## Slide 7: Proposal
NR should target to support non-orthogonal multiple access in UL at least for mMTC
In the UL LLS evaluation of non-orthogonal multiple access for mMTC, it is recommended to consider the following
    MA signature (e.g., code, codebook, sequence, interleaver, etc) collision
    Channel correlation between UEs
      FFS detailed channel correlation model