## Slide 1: WF on DCI for PC5-based V2V with mode-1
CMCC, OPPO, ITRI, Samsung, NTT DoCoMo, Qualcomm, Huawei, HiSilicon, Xinwei, ZTE,
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden 22nd - 26th August 2016 Agenda item 7.2.2.4.1
R1-16xxxx

## Slide 2: Proposal
For PC5-based V2V with mode-1, DCI size is common for dynamic and SPS scheduling.
At least the following fields are included in the DCI format for dynamic scheduling
  CIF
  Resource for PSCCH
  SA content (can be copied from SCI field)
    Frequency hopping flag
    frequency Resource indicator
    Time resource indicator
At least the following contents are included in the DCI for SPS scheduling
  CIF
  SPS process indication
  SPS status(active/release)
  FFS: Resource for PSCCH
  FFS: SA content (can be copied from SCI field)
    Frequency hopping flag
    frequency Resource indicator
    Time resource indicator