## Slide 1: Evaluation Scenarios and Assumptions for DL and UL Mobility
Qualcomm Incorporated, Huawei, Intel
3GPP TSG RAN WG1 #86 R1-168488
Gothenburg, Sweden, 22nd- 26th August 2016
Agenda item: 8.1.6

## Slide 2: Background
In the context of the ongoing Rel-14 RAN study, various performance KPIs and requirements have be proposed in the latest 38.913, including UE energy efficiency, mobility and Network energy efficiency, etc.
UL based mobility has potential to improve some KPIs compared to DL based mobility
This evaluation is targeting scenarios where UL based mobility could complement DL based mobility

## Slide 3: Proposed Evaluation Scenarios
Dense Urban
  Macro only (<=60 km/h)
  2-layer (<=30 km/h)
  Low mobility case is not precluded
Rural with high speed UEs
High Speed Train
Urban Macro (optional)
Other scenarios could be added

## Slide 4: System-level evaluation assumptions
Dense Urban
Parameters | Dense urban
Layout | Two layer Macro layer: Hex. Grid Micro layer: Random drop 9 micro BSs per macro BS
Inter-BS distance | Macro layer: 200m
Carrier frequency | 4 GHz
Simulation bandwidth | 20MHz per CC
Channel model | 3D UMa (Macro layer) and 3D UMi (Micro layer)
BS Tx power | Macro layer 44 dBm PA scaled down with simulation BW when system BW is higher than simulation BW. Otherwise, 44 dBm Micro layer: 33dBm for 20MHz system bandwidth when system BW is higher than simulation BW. Otherwise, 44 dBm.
BS antenna configurations | (8,1,2) with directional antenna element (HPBW=650, directivity 8dB) other values are not precluded
UE Tx power | 23dBm
UE antenna configurations | (1,1,2) with omni-directional antenna element other values are not precluded
BS antenna height | 25m for macro cells and 10m for micro cells
UE antenna height | 1.5m
UE distribution | 10 users per macro TRP, 10 users per micro TRP 100% outdoor,30km/h (basleine), 3, 60 km/h (optional) Simultaneous UEs within a slot UE location/movement direction randomly chosen
BS receiver noise figure | 5dB
UE receiver noise figure | 9dB
UE s receiver | Realistic
Network Synchronization | Synchronized TRPs . Asynchronized TRPs FFS.

## Slide 5: System-level evaluation assumptions
Rural with high speed UEs
Parameters | High Speed Rural
Layout | Single layer Macro layer: Hex. Grid
Inter-BS distance | 1732m
Carrier frequency | 4GHz
Simulation bandwidth | 20MHz per CC
Channel model | 3D UMa
BS Tx power | 49dBm PA scaled down with simulation BW when system BW is higher than simulation BW. Otherwise, 49dBm
BS antenna configurations | (8,1,2) with directional antenna element (HPBW=650, directivity 8dB) other values are not precluded
UE antenna configurations | (1,1,2) with omni-directional antenna element other values are not precluded
UE Tx power | 23dBm
BS antenna height | 35 m
BS receiver noise figure | 5 dB
UE receiver noise figure | 9 dB
UE distribution | Outdoor vehicles 120km/h 10 UEs per TRPs UE location/movement direction randomly chosen
BS receiver noise figure | 5dB
UE receiver noise figure | 9dB
UE and BS receiver | Realistic
Network Synchronization | Synchronized TRPs . Asynchronized TRPs FFS.

## Slide 6: System-level evaluation assumptions
Highs Speed Train
Parameters | High Speed Train
Layout | Follow 38.913
Inter-BS distance | 1732m
Carrier frequency | 4GHz, other frequency not precluded
Simulation bandwidth | 20MHz per CC
Channel model | ITU Rural
BS antenna configurations | (8,1,2) with directional antenna element (HPBW=650, directivity 8dB) other values are not precluded
BS Tx power | 49dBm
UE antenna configurations | (1,1,2) with omni-directional antenna element other values are not precluded
UE Tx power | 23dBm
UE distribution | 1000 UEs per train and 30% active UEs 100% of users in train at 480 km/h Each company should open how to model NW configuration
BS receiver noise figure | 5dB
UE receiver noise figure | 9dB
UE and BS receiver | Realistic
Network Synchronization | Synchronized TRPs . Asynchronized TRPs FFS.

## Slide 7: Link Level Evaluation and Link to System Mapping
Link to system mapping is needed to ensure accurate modelling of the receiver performance in SLS
  Interference from/to UEs with timing/frequency inaccuracy should be considered
    Candidate solution: Explicit modeling of waveform transmission and reception in the SLS
    Other solutions are not precluded
Companies are encouraged to provide link simulation results and clarify link to system mapping
  Companies are encouraged to provide power control algorithm description
    E.g., UL open-loop power control based on DL measurements

## Slide 8: Link-level evaluation assumptions
 | SYNC (PSS/SSS/PBCH, other options) | Uplink Energy Efficient Signal (SRS/PRACH, other options)
Carrier Frequency | 4 GHz | 
Channel Model | CDL-C with scaling 100ns (UE Speed 30 km/h, 60 km/h, 120 km/h, 480 km/h), AWGN | 
Subcarrier Spacing(s) | Companies report | 
SNR range | ≥ -6dB | Companies report range
Receiver Search Window | The time window to search (correlate) NR-PSS. It depends on the periodicity of NR-SS transmission. The value needs to be provided by each proponent | Search window covering timing uncertainty derived from cell radius, when UE is not in the connected RRC state
Antenna Configuration at the TRP | (1,1,2) with omni-directional antenna element | (1,1,2) with omni-directional antenna element
Antenna Configuration at the UE | (1,1,2) with omni-directional antenna element | (1,1,2) with omni-directional antenna element
Antenna port virtualization | Clarified by each proponent in simulation assumptions (e.g. the beamforming method, beam directions, number of beams) | 
Frequency Offset | Initial acquisition TRP: uniform distribution +/- 0.05 ppm UE: uniform distribution +/- 5, 10, 20 ppm (each company to choose one) Non-initial acquisition TRP: uniform distribution +/- 0.05 ppm UE: uniform distribution +/- 0.1 ppm | TRP: uniform distribution +/- 0.05 ppm UE: uniform distribution +/- 0.1 ppm
Number of interfering TRPs | 1. 0 TRP: mandatory 2. 2 interfering TRPs (1st SIR = 0dB, 2nd SIR = -3dB; SIR is defined as the ratio of power between a reference cell and interfered cell) – timing arrival differences from TRPs are provided by each proponent: optional | N/A
Number of interfering UEs | N/A | 1. 0 UE: mandatory 2. 2 interfering UEs (1st SIR = 0dB, 2nd SIR = -3dB; SIR is defined as the ratio of power between a reference UE and interfered UEs)

## Slide 9: Performance metrics
System level simulations
  Resource efficiency
    Time-freq resource usage of signals used for DL/UL based measurement and paging resource (e.g., number of TRPs involved in paging a UE )
  Handover failure rate
  Paging miss rate
  UE battery life with relative power model between DL and UL mobility
  Signaling load (ping-pong, # of HOs)
Link level simulations
  Signal detection performance (misdetection, false alarm)
  Measurement accuracy (signal level)
Other metrics are not precluded, e.g. mobility interruption time