## Slide 1
WF on SLS evaluation methodologies for MA
LG Electronics, ZTE, ZTE Microelectronics
R1-168510
3GPP TSG RAN WG1 #86
Gothenburg, Sweden, 22nd – 26th August 2016
Agenda item 8.1.2.2

## Slide 2: Background – offline discussion results
UL traffic model for mMTC applied to MA is as follows :
Attributes | Value or assumptions
Data packet arrival rate per UE | Poisson arrival with arrival rate λ
Number of UEs per cell | Companies report the number of UEs per cell
Packet size | Option 1: Follow TR45.820 Option 2: Fix 40 Bytes Companies are encouraged to evaluate both options Option 1: Fix: [20, 40,] Bytes (Company reports the used value) Option 2: Variable, e.g., traffic model in NB-IoT Option 3: Random [20, 40, 200] Bytes Other option is not precluded Select option at RAN#86bis Companies report details on packet segmentation assumption
Simulation Bandwidth | Companies report the simulation bandwidth
Target packet drop rate | 0.01
Packet dropping timer | Baseline: 1s, 10s Other values are not precluded.

## Slide 3: Background-offline discussion results
  For the SLS evaluation for autonomous/grant-free/contention-based UL MA applied to mMTC,
  At least following performance metrics are used
  Companies report
    packet drop rate vs. packet arrival rate per cell curve
  Traffic model with Poisson arrival is used
    Companies are encouraged to report payload size used in the simulation
  At least following performance metrics are used
    Packet drop rate vs. packet arrival rate per cell curve
      Target packet drop rate for comparison of MA schemes is 0.01
      Companies are encouraged to provide packet dropping criteria
    Number of UEs per cell used in the simulation should be reported
    Note: packet arrival rate reflects system loading, e.g. number of arrived packets per cell per sec.

## Slide 4: Proposal
UL traffic model for mMTC applied to MA is as follows :
Attributes | Value or assumptions
Data packet arrival rate per UE | Poisson arrival with arrival rate λ
Number of UEs per cell | Companies report the number of UEs per cell
Packet size | Option 1: Follow TR45.820 Option 2: Fix 40 Bytes Companies are encouraged to evaluate both options Companies report details on packet segmentation assumption
Simulation Bandwidth | Companies report the simulation bandwidth
Target packet drop rate | 0.01
Packet dropping timer | Baseline: 1s, 10s Other values are not precluded.

## Slide 5: Proposal
  For the SLS evaluation for grant-free UL MA applied to mMTC,
  Companies report
    packet drop rate vs. packet arrival rate per cell curve