## Slide 1: WF on Battery Life Evaluation Methodology for mMTC
Qualcomm Incorporated
3GPP TSG RAN WG1 #86 R1-168517
Gothenburg, Sweden, 22nd- 26th August 2016
Agenda item: 8.1.7

## Slide 2: Background
RAN requirement for battery life evaluation
UE battery life can be evaluated by the battery life of the UE without recharge. For mMTC, UE battery life in extreme coverage shall be based on the activity of mobile originated data transfer consisting of 200bytes UL per day followed by 20bytes DL from MCL of 164dB, assuming a stored energy capacity of 5Wh.
The target for UE battery life should be beyond 10 years, 15 years is desirable.

## Slide 3: Proposal
UE power consumption model
  Based on email discussion

## Slide 4: Proposal
Protocol flow

## Slide 5: Proposal
Duration for each protocol flow
Steps | Purpose | UE Power Mode | Durations @ MCL164dB | Notes
S1 | SYNC reading | Receive | 200ms | 
S2 | MIB/SIB1/SIB2 reading | Receive | 500ms | 
S3 | RACH | Transmit | 500ms | 
S4/S5/S8 | RACH contention resolution + PDCCH UL grant | Receive | 250ms | 
S6/S9 | 200 Byte UL packet trans. | Transmit | Based on LLS | Both the PA back off due to waveform PAPR and the channel estimation need to be captured.
S7/S10 | DL MAC ACK | Receive | 64ms | 
S11 | PDCCH DL grant | Receive | 280ms | 128ms for each PDCCH, 1.1 PDCCH for DL and 1.1 PDCCH for UL
S12 | 20 Byte DL application ACK trans. | Receive | 333ms | Assume DL 3:1 UL @~480bps
S13 | UL MAC ACK | Transmit | 128ms | 
- | Sleep between S1-S13 | Sleep | 500ms | 

## Slide 6: Proposal
Duration of the protocol flow is provided by LLS, at least for transmission of UL packet, considering the PA back off due to PAPR of the chosen waveform, channel estimation, demod loss.

## Slide 7: Proposal
Traffic model for battery life evaluation
200 bytes UL per day followed by 20bytes DL from MCL of 164dB, assuming a stored energy capacity of 5Wh.