## Slide 1: WF on Additional Penetration Loss Model for mMTC
Qualcomm Incorporated
3GPP TSG RAN WG1 #86 R1-16xxxx
Gothenburg, Sweden, 22nd- 26th August 2016
Agenda item: 8.1.7

## Slide 2: Background
In RAN1 #85 the following simulation SLS assumption is agreed for mMTC
Attributes | Values or assumptions
Layout | Single layer - Macro layer: Hex. Grid
Inter-BS distance | 1732m
Carrier frequency | 700MHz
Simulation bandwidth | Companies report simulation bandwidth used in evaluation
Channel model | 3D UMa Take 5GCM output into account if applicable.
Tx power | UE: Max 23dBm or optional 10dBm
BS antenna configuration | Rx: 2 and 4 ports (8 as optional)
BS antenna pattern | Follow the modelling of TR36.873
BS antenna height | 25m
BS antenna tilt | Companies report tilt
BS antenna element gain + connector loss | 8 dBi, including 3dB cable loss
BS receiver noise figure | 5 dB
UE antenna elements | 1Tx
UE antenna height | 1.5m
UE antenna gain | -4dBi
Traffic model | Non-full buffer small packet. Consider future trend of mMTC traffic
UE distribution | 20% of users are outdoor in cars (100km/h) or 20% of users are outdoors (3km/h) 80% of users are indoor (3km/h) Users dropped uniformly in entire cell
BS receiver | MMSE-IRC as baseline, Advanced receiver is not precluded
UL power control | Companies report power control scheme
Channel estimation | Realistic

## Slide 3: Background
The agreed path loss model 3D UMa is not enough to address the requirement for mMTC, MCL 164dB

## Slide 4: Proposal
Follow NBIoT to introduce additional penetration loss to meet RAN requirement:
Path loss indoor = path loss computed in 3D UMa + additional Penetration Loss
Calibration between companies to ensure path loss tail is 164dB

## Slide 5: Proposal
Building Penetration Loss = Scaling * (External wall penetration loss + max (Tor1, Tor3) – GFH)
Scaling = 0.42
Tor1 = Wi*p, where Wi is the loss in internal walls and p is the number of penetrated internal walls.
Wi = 4-10 dB (uniformly distributed)
p =0, 1, 2 or 3 (with p =3 also accounting for devices in deep penetration loss e.g. basement)
Tor3 = alpha*d, where alpha is the penetration distance coefficient and d is the penetration distance.
Penetration distance coefficient (alpha) = 0.6 dB/m
d = uniformly distributed in the range 0-15m
GFH = n*Gn, where Gn is the floor height gain per floor, n is the floor number
n = 0,1,2,3 or 4 (uniform distribution)
Gn = 1.5 dB/floor
External wall loss is modelled as uniformly distributed either in range 4-11 dB, 11-19 dB or 19-23 dB.

## Slide 6: Proposal
Distribution of external wall penetration loss |  |  | 
External wall penetration loss | 4-11 dB | 11-19 dB | 19-23 dB
Percentage of devices uniformly distributed in range | 25% | 50% | 25%
Assumptions related to additional penetration loss due to internal walls |  |  | 
Percentage of devices mapped to case p=3 ( with remaining devices equally distributed among cases p=0,1,2) | 20% |  | 
Assumption for dependency of penetration loss of internal walls of a building. | Dependent i.e. one value of Wi is randomly generated and applies to all internal walls. |  |