## Slide 1: Way forward on slot alignment
Huawei, HiSilicon, MediaTek
3GPP TSG RAN WG1 #86 R1-168524
Gothenburg, Sweden, August 22-26, 2016
Agenda item: 8.1.3.1

## Slide 2: Case of same CP overhead
In case of the same CP overhead with different subcarrier spacings and symbol alignment, slot boundaries of 15 kHz and 2^m*15 kHz must be aligned:
Without slot alignment there is no symbol alignment *
* Independently of defining slot as 7 or 14 symbols

## Slide 3: Case of different CP overhead
0.5ms/1ms
15KHz
30KHz
60KHz
0.25/0.5
0.125/0.25
Slot alignment among different CP overheads with different subcarrier spacings
Examples:
- 15/30/60kHz have different CP overheads below

## Slide 4: Proposal
For CP overheads larger than zero, if a slot is agreed to be 7 and/or a multiple of 7 symbols for normal CP, slot boundaries are aligned at the subframe boundary in case of:
  different CP overheads with the same subcarrier spacing
  different CP overheads with different subcarrier spacings
FFS CP overhead equals to zero
Add to the working assumption on symbol alignment:
  Slot boundaries of different numerologies with the same CP overhead are aligned at the subframe boundary.