## Slide 1: WF on scenario and channel model for NR MIMO link and system level calibration
3GPP TSG RAN WG1 Meeting #86 R1-168529
Gothenburg, Sweden, 22nd – 26th August 2016
Agenda Item: 8.1.5
ZTE Corporation, ZTE Microelectronics

## Slide 2: Background
  RAN1 agreements
  For the purpose of calibration, companies are encouraged to provide baseline results for NR MIMO in the following meetings, including link-level and system level simulations
    Discuss further on baseline simulation assumptions and metrics for calibration in email discussion after RAN1#86
    Thereafter, email reflector is used to collect results (no online time for calibration discussions, similar to channel model calibration)

## Slide 3: Proposals
  Approve the following scenario/channel model for NR MIMO link and system levels calibration:
  Link-level: CDL model with random angular offset, e.g.,
      3GPP TR38.900 CDL-A model (Delay spread = 10 ns )
      3GPP TR38.900 CDL-D model (Delay spread = 10 ns )
      Mobility: 3km/h
      Notes: The angles are uniformly distributed within 0-360 degrees in azimuth domain and 0-180 degrees in zenith domain via applying uniform-distribution translation angle in Section 7.7.5.1 in TR 38.900 accordingly.
  System-level: Indoor hotspot, Urban macro, dense urban