## Slide 1: WF on UL DMRS for sTTI
Huawei, HiSilicon, Nokia, ASB, Ericsson, Potevio, Qualcomm, CATT, Intel, Spreadtrum, LG, Mediatek, Samsung, ZTE, ZTE Microelectronics, NTT DOCOMO, Panasonic,Sony
3GPP TSG RAN WG1 #86 R1-168533
Gothenburg, Sweden 22nd - 26th August 2016
Agenda item: 7.2.12.2.1

## Slide 2: Proposals
At least for 2-symbol based sTTI, UL DMRS position for sPUSCH is indicated by eNB
  FFS how to indicate UL DMRS position
  FFS whether or not to support fixed UL DMRS position
For 1-slot sTTI, self-contained UL DMRS for sPUSCH is supported
  Support at least the legacy DMRS structure, where DMRS is located in the fourth symbol of the slot