## Slide 1: WF on NR MIMO calibration
3GPP TSG RAN WG1 Meeting #86 R1-167962
Gothenburg, Sweden, 22nd – 26th August 2016
Agenda Item: 8.1.5
ZTE Corporation, ZTE Microelectronics, Intel Corporation, Samsung

## Slide 2: Background-1
  Multi-beam approaches with different types of beamforming including analog/digital/hybrid beamforming are discussed in RAN1.
  Before launching the performance evaluation for new multi-beam approaches, it is desirable to have companies to calibrate their simulation platforms of multi-beam link/system levels with each other so that the group has a common ground.
  Meanwhile, discussion about this calibration has been launched in last RAN1#85 Nanjing meeting. Antenna-configuration-related parameters in agreements have been highlighted to be used for calibration as in the following slide:

## Slide 3: Background-2
 | Below 6GHz (700MHz, 4GHz) | Above 6GHz (30GHz, 70GHz)
BS (M,N,P,Mg,Ng) | Mg=1,Ng=1 Other configurations are FFS 4GHz: Dense urban and Urban macro: - Baseline: (M,N,P,Mg,Ng) = (8,8,2,1,1). - Note that for Urban macro, companies are also encouraged optionally to investigate larger panels, e.g. (8,16,2,1,1) Indoor hotspot: - FFS Baselines are at least for MIMO-related calibration (and can also be used for other features unless a different baseline is defined for evaluation of a particular feature). Companies are encouraged to evaluate other configurations as well. | FFS 30GHz: Dense urban and Urban macro: - Baseline: (M,N,P,Mg,Ng) = (4,8,2,2,2). Indoor hotspot: - FFS 70GHz: Dense urban: - Baseline: (M,N,P,Mg,Ng) = (8,16,2,2,2). Indoor hotspot: - FFS Baselines are at least for MIMO-related calibration (and can also be used for other features unless a different baseline is defined for evaluation of a particular feature). Companies are encouraged to evaluate other configurations as well.
BS (dH,dV,dH,g,dV,g) | (0.5,0.8, FFS, FFS) Other value dv is FFS 4GHz: Dense urban and Urban macro: - Baseline: (dH,dV) = (0.5, 0.8)λ. Indoor hotspot: - FFS Baselines are at least for MIMO-related calibration (and can also be used for other features unless a different baseline is defined for evaluation of a particular feature). Companies are encouraged to evaluate other configurations as well. | (0.5,FFS, FFS, FFS) 30GHz: Dense urban and Urban macro: - Baseline: (dH,dV) = (0.5, 0.5)λ. (dg,H,dg,V) = (4.0, 2.0)λ. - Note that companies are also encouraged to investigate a larger panel spacing, e.g. (dg,H,dg,V) = (8,4)λ Indoor hotspot: - FFS 70GHz: Dense urban: - Baseline: (dH,dV) = (0.5, 0.5)λ. (dg,H,dg,V) = (8.0, 4.0) λ. - Note that companies are also encouraged to investigate a larger panel spacing, e.g. (dg,H,dg,V) = (16,8) λ Indoor hotspot: - FFS Baselines are at least for MIMO-related calibration (and can also be used for other features unless a different baseline is defined for evaluation of a particular feature). Companies are encouraged to evaluate other configurations as well.

## Slide 4: Proposals-1
  RAN1 starts NR MIMO calibration to reach common ground for MIMO related evaluation:
  Link-level calibration
      Support the subsequent link-level evaluation for candidate designs/approaches, e.g., reference signals;
      Calibration assumptions and metrics are FFS;
  System-level calibration
      Support the subsequent system-level evaluation for candidate designs/approaches, e.g., multi-beam sweeping/ selection/reporting;
      Calibration assumptions and metrics are FFS;

## Slide 5: Proposals-2
  Approve the following scenario/channel model for link and system levels calibration:
  Link-level: CDL model with random angular offset, e.g.,
      3GPP TR38.900 CDL-A model (Delay spread = 10 ns )
      3GPP TR38.900 CDL-D model (Delay spread = 10 ns )
      Mobility: 3km/h
      Other details FFS
      Notes: The angles should be wrapped around to be uniformly within 0-360 degrees in azimuth and clipped within 0-180 degrees in zenith angle via applying uniform-distribution translation angle in Section 7.7.5.1 in TR 38.900 accordingly.
  System-level: Indoor hotspot, urban macro, dense urban
    Other details FFS