## Slide 1
3GPP TSG RAN WG1 Meeting #86 R1-167964 Gothenburg, Sweden, 22nd - 26th Aug 2016
Agenda item: 8.1.5
WF on DL Transmission Scheme
Huawei, HiSilicon, NEC

## Slide 2: Background
In RAN1#85 meeting, the following agreements were achieved,
The following DL multi-antenna transmissions to be studied for NR
  Closed-loop/(Semi)Open-loop spatial multiplexing
  Single/Multi-point transmissions
  SU/MU-MIMO
  Transmit diversity,
    e.g., Single/Multi panel spatial diversity
  Combination of above techniques
Other DL multi-antenna transmissions and related techniques are not precluded
This does not imply that used transmission technique needs to be known to the UE

## Slide 3: Proposal
NR should support the multiplexing of different transmission schemes to different UEs at the same time-frequency resource (an example is shown by Figure 1)
NR should support beam based transmit diversity
  Beam based transmit diversity based on single-TRP transmission should be supported in NR
  Beam based transmit diversity based on multi-TRP transmission should be supported in NR (an example is shown by Figure 2)
  Beam based transmit diversity is based on DM-RS for demodulation
Beam based transmit diversity should be the fallback scheme of the multi-antenna based transmission mode
The dynamic switching between different transmission schemes should be supported in a transmission mode

## Slide 4
Figure 1. Multiplexing of different transmission schemes to different UEs at the same time-frequency resource.
Figure 2. Beam based transmit diversity based on multi-TRP transmission.