## Slide 1: WF on Class A CSI-RS Enhancement
CATT, Alcatel-Lucent Shanghai Bell, Intel, InterDigital, Nokia, Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden 22nd - 26th August 2016
Agenda item: 7.2.4.1.1
R1-168049

## Slide 2: Background
Conclusions from RAN1#85
  Further discussion till RAN1#86, especially regarding evaluating different alternatives, e.g., using OCC 2/4/8, high reuse of CSI-RS, etc.
Observations from system-level simulation results
  System-level simulation
    R1-166439: CDM-8 vs. CDM-2
      CDM-8 achieves up to 57% cell-edge throughput gain over CDM-2
    R1-167634: CDM-8 vs. CDM-4
      For reuse-1, cell-edge throughput gain of 20-24% and mean throughput gain of 7-8%
      For reuse-3, cell-edge throughput gain of 14-20% and mean throughput gain of 5-7%
  Link-level simulation:
    R1-166269, R1-166519

## Slide 3: Proposal
CDM-8 is supported for at least {24,32} port CSI-RS
  FFS CSI-RS aggregation and CDM mapping details
  FFS additional REs other than legacy CSI-RS RE