## Slide 1: WF on UL DMRS enhancement
Intel Corporation
R1-168050
3GPP TSG RAN1 #86
Gothenburg, Sweden, 22nd – 26th August 2016
Agenda Item: 7.2.4.1.3

## Slide 2: Background
Major drawback of IFDMA based approach
  Cannot support MU-MIMO with legacy UE
  New sequence generation, e.g. one PRB RPF=2, 1/2/3 PRBs RPF=4
  Channel estimation loss for high rank large delay spread

## Slide 3: Proposal
RAN1 to specify block wise ZC sequence for UL DMRS enhancement
  When enabled, DMRS sequence is generated using two/three ZC sequences and each is applied to one contiguous block of PRBs
  High layer signaling or L1 signaling to indicate sequence generation, i.e. whether legacy sequence generation or new sequence generation is applied