## Slide 1: WF on TTI bundling for PUSCH in UpPTS
CMCC, NEC
R1-168098
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, August 22–26, 2016
Agenda item 7.2.9

## Slide 2: Background
In RAN#71, a new Work Item on Uplink Capacity Enhancements for LTE was approved, aiming for enhancing the uplink capacity of LTE by means of introducing uplink 256QAM, and supporting PUSCH transmission in UpPTS
The objectives of the work of PUSCH in UpPTS that related to RAN1 include
  Specify mechanism for supporting PUSCH transmission in special subframe with DwPTS of 6 OFDM symbols, GP of 2 OFDM symbols.
  Backward compatibility with legacy UEs is maintained
In current specification, only TDD configuration 0, 1, 6 support uplink TTI bundling, since the TTI bundling requires at least four UL TTI in a radio frame. When PUSCH transmission in UpPTS is allowed, it provide opportunity for TDD configuration 2 and configuration 3 to support TTI bundling.

## Slide 3: Proposals
Support TTI bundling for TDD configuration 2 and 3 when supporting of PUSCH in UpPTS
Specify the scheduling and HARQ timing for TTI bundling as follows
  The UE shall upon detection of a PDCCH with DCI format 0 in subframe n intended for the UE, adjust the corresponding PUSCH transmission in subframe n+k, with k in the following table
  For scheduled PUSCH transmissions in subframe n, which corresponds to the last TTI in the bundle, a UE shall determine the corresponding PHICH resource in subframe n+k_phich, with k_phich in the following table
TDD UL/DL Configuration | DL subframe number n |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
2 |  | 5 |  | 4 |  |  | 5 |  | 4 | 
3 | 4 |  |  |  |  |  |  | 4 | 4 | 4
TDD UL/DL Configuration | DL subframe number n |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
2 |  | 4 | 6 |  |  |  | 4 | 6 |  | 
3 |  | 4 | 6 | 6 | 6 |  |  |  |  | 

## Slide 4: Proposals
Specify the scheduling and HARQ timing for TTI bundling as follows(cont’)
  The UE shall upon detection of a PHICH transmission intended for the UE in subframe n-l, adjust the corresponding first PUSCH transmission in the bundle in subframe n+k, with l in the following table
Specify the number of HARQ processes for subframe bundling operation under TDD configuration 2 and 3 as in the following table
TDD UL/DL Configuration | DL subframe number n |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
2 |  | 3 |  | 3 |  |  | 3 |  | 3 | 
3 | 1 |  |  |  |  |  |  | 7 | 3 | 1
TDD UL/DL configuration | Number of HARQ processes for subframe bundling operation
2 | 2
3 | 2