## Slide 1: WF on URLLC Evaluation Metric
Intel
3GPP TSG RAN WG1 Meeting #86 R1-168131
Gothenburg, Sweden, 22nd - 26th August 2016
Agenda item - 8.1.7

## Slide 2: Background
At RAN1#85, URLLC system capacity C(L, R) was agreed as an evaluation metric
Depending on system settings (e.g. BW, TTI duration etc.) it may not be feasible to serve outage UEs with bad channel propagation conditions (e.g. due to link budget limitation)
  Outage UEs are terminals that cannot provide target reliability within latency limits for certain system configuration settings or URLLC transmission scheme
Outage UEs should be taken into account in evaluations of URLLC system capacity C(L, R)

## Slide 3: Background
The following alternatives can be considered to take into account outage UEs in evaluation:
  Alt 1. Agree on target MCL assumed for URLLC evaluation and perform admission control e.g. re-drop a UE if its channel propagation conditions does not satisfy agreed MCL.
    In this approach, it is uncertain whether the fraction of such UEs is allowed to be more than the target error rate (1-R)
  Alt 2. Include such users into statistics by defining additional metrics for URLLC evaluation

## Slide 4: Proposal
Additionally to the system URLLC capacity C(L, R), define an observed URLLC system reliability SR and outage (1-SO) metric for the given (Λ, L, R)
  Λ – offered traffic load in the cell
  L – latency target
  R – reliability target