## Slide 1: WF on alignment among different numerologies
LG Electronics, Intel, Ericsson, Qualcomm, Samsung, Verizon,
3GPP TSG RAN WG1 Meeting #86 R1-168305
Gothenburg, Sweden, 22nd - 26th Aug 2016
Agenda Item: 8.1.3.1

## Slide 2: Background
Alignment of subframes
  [Note] subframe definition agreed in RAN1#86
    A subframe duration is defined by the duration of x OFDM symbols given a reference numerology
    With the same CP overhead, a single value of x is specified irrespective of the subcarrier spacing value chosen for the reference numerology
  [Note] agreed in RAN1#85
    For the numerology with 15 kHz and larger subcarrier spacing ,1 msec alignment is supported

## Slide 3: Proposals
Alignment of subframes
  Subframe duration in ms for a subcarrier spacing (2m*15)kHz is exactly 2-m times the subframe duration for 15 kHz subcarrier spacing
Alignment within a subframe
  Symbol level alignment across different subcarrier spacings with the same CP overhead is assumed when they are multiplexed in a TDM manner within a subframe duration in a NR carrier

## Slide 4: Proposal
For normal CP family, choose one option from the followings for symbol-level alignment
  For Fs = F0 * 2n (n is a positive integer, F0 = 15 kHz),
    Each symbol length (including CP) of F0 equals the sum of the corresponding 2n symbols of Fs
      Option 1: The first 2n symbols of Fs have equal symbol length
      Option 2: Except for the first symbol of Fs , all symbols of Fs have equal symbol length. The length of first symbol of Fs is sum of length of the second symbol and 0.51 us
        Option 2-1. 0.51us can be reserved, and all symbols have the equal length

## Slide 5: Example
Symbol level alignment Option 1
Symbol level alignment Option 2

## Slide 6: Example
Symbol level alignment Option 2-1
Slot/subframe level alignment