## Slide 1: Definitions supporting beam related procedures
Nokia, Qualcomm, CATT, Intel, NTT DoCoMo, Mediatek, Ericsson, ASB, Samsung, LG
3GPP TSG RAN WG1 #86 R1-168322
Gothenburg, Sweden, Aug 22 - 26, 2016
8.1.5

## Slide 2: Background
Figure: A taxonomy of procedures
Beam Related Procedures
Mobility (L3)
Beam Management (L1/L2 based)
Scope of the WF

## Slide 3: Proposals
Beam management = a set of procedures to acquire and maintain a set of TRP(s) and/or UE beams that can be used for DL and UL transmission/reception, which include at least following aspects:
  Beam selection= for TRP(s) or UE to select of its own beam(s).
  Beam measurement = for TRP(s) or UE to measure characteristics of received beamformed signals
  Beam reporting = for UE to report a property/quality of beamformed signal(s) based on beam measurement
  Beam sweeping = operation of covering a spatial area, with beams transmitted and/or received during a time interval in a predetermined way.