## Slide 1: WF on Supporting URLLC in NR
LG Electronics, ZTE, Sharp, MTI,
3GPP TSG RAN WG1 Meeting #86 R1-168550
Gothenburg, Sweden, 22nd - 26th Aug 2016
Agenda Item: 7.1.3.2

## Slide 2: Proposal
At least the following potential options should be considered
  At least for shorter transmission UL, semi-static resource sharing between URLLC and eMBB
    FDM and/or TDM manner
      Note: UL grant-free transmission for URLLC can be considered
      Other schemes are not precluded
  Dynamic resource sharing between URLLC and eMBB
    For DL, mechanisms to schedule a transmission where the resources of it can overlap with resources of ongoing/scheduled longer transmission at least from network perspective
      FFS: A similar or same mechanism applicability to UL
      Note: preemption or superposition can be considered
    Scheduling based approaches (e.g., by adapting transmission duration or by using different subbands) to allow multiplexing of different durations of transmission
    UL grant-free transmission for URLLC
    Other schemes are not precluded
  Other mechanisms are not precluded