## Slide 1: Way Forward on UE-specific slot configuration
CATT
3GPP TSG RAN WG1 #86bis
Lisbon, Portugal, October 10th – 14th 2016
R1-1608762

## Slide 2: Background
In RAN1#86, Followings are considered as starting points of NR frame structure at least within the CP overhead
  Subframe
    Already agreed upon
    Assume x=14 in the reference numerology for subframe definition (for normal CP)
    FFS: y=x and/or y=x/2 and/or y is signalled
  Slot
    Slot of duration y OFDM symbols in the numerology used for transmission
    An integer number of slots fit within one subframe duration (at least for subcarrier spacing is larger than or equal the reference numerology)
    The structure allows for ctrl at the beginning only
    The structure allows for ctrl at the end only
    The structure allows for ctrl at the end and at the beginning
    Other structure is not precluded
    One possible scheduling unit
  Mini-slot
    Should at least support transmission shorter than y OFDM symbols in the numerology used for transmission
    May contain ctrl at the beginning and/or ctrl at the end
    The smallest mini-slot is the smallest possible scheduling unit (FFS: smallest number of symbols)
  Note: the names are for the purpose of discussion. Whether some terms can be merged or not is FFS
  FFS whether NR frame structure needs to support both slot and mini-slot or these can be merged

## Slide 3: Proposals:
Multiplexing of UEs in the dynamic TDD structure without gap
  UE’s slot are UE-specifically configured for eMBB and URLLC UEs
  The starting symbol of a slot is configured with N-symbol offset relative to the boundary of a subframe.
DL
UL
GP
Slot
DL
UL
GP
DL
UL
GP
DL
UL
GP
eMBB UE1
eMBB UE2
Subframe i
Slot offset related subframe boundary
DL
UL
URLLC UE
Small URLLC schedule interval for low latency
DL
UL
GP
GP