## Slide 1: WF on Symbol Level Alignments
LG Electronics, NTT DOCOMO, Ericsson, Panasonic, Qualcomm, ZTE
3GPP TSG RAN WG1 Meeting #86bis R1-1610652
Lisbon, Portugal, 10th - 14th October
Agenda Item: 8.1.2.1

## Slide 2: Background
Working assumption:
  Alignment within a subframe
    Symbol level alignment across different subcarrier spacings with the same CP overhead is assumed within a subframe duration in a NR carrier
    FFS: Unlicensed spectrum case

## Slide 3: Proposal
Confirm WA in the background
For normal CP family, the following is adopted
  For Fs = 15 kHz * 2n (n is a positive integer),
    Each symbol length (including CP) of 15 kHz equals the sum of the corresponding 2n symbols of Fs
    Other than the first OS in every 0.5msec, all OFDM symbols within 0.5msec have the same size
    The first OS in 0.5msec has longer CP of 16 Ts (assuming 15 kHz and FFT size of 2048) compared to other OSs
  For Fs = 15 kHz * 2n (n is a negative integer)
    Each symbol length (including CP) of Fs equals the sum of the corresponding 2n symbols of 15 kHz

## Slide 4: Example
First 7 symbols for of SCS supported by NR for NCP case