## Slide 1: Discussion points on Downlink Control Signaling
Ericsson
R1-10683
8.1.7.1

## Slide 2: Discussion Points
Downlink control channels
  “PDCCH” for downlink scheduling assignments/grants
  Other types of control channels to be discussed/motivated
Need for beamforming support?
  Can we agree on “yes, need to support UE-specific beamforming of downlink control”?
  Impact on broadcast-type channels (e.g. PCFICH)?
  Impact on RS structure? Individual DM-RS per PDCCH vs shared RS?
  Tx diversity when beamforming is not desirable/possible? Spec-transparent vs specified?

## Slide 3: Discussion Points
Frequency dimension – BW for control channels cannot span full system BW
  Introduce some form of “subband”/”control region in the frequency domain”?
  Size? Integer number of RBs? How to now where it is located?
Time dimension
  Control signaling located at the first OFDM symbol(s) of a slot (or mini-slot)?
  Size of control region – one or multiple OFDM symbols? Semi-static or dynamically varying?
  One PDCCH spans one OFDM symbol vs multiple OFDM symbols?
  Support for FDM between data and control (“PDSCH” and “PDCCH”) or adopt TDM only?
  Single-stage (like LTE) vs multi-stage PDCCH (first DCI points to the remaining DCI)?

## Slide 4: Discussion Points
DCI timing
  Same-slot (DCI and DL data in same slot)
  Cross-slot (DCI and DL data in different slots)?
  Same-slot (DCI and UL data in same slot)?
  Cross-slot (DCI and UL data in different slots)?
Blind decoding and DCI formats
  Should we try to clean up the LTE DCI format structure? Limited number of DCI sizes?
  Search space design?