## Slide 1: WF on HARQ timing for PUSCH in UpPTS
CMCC
R1-1610695
3GPP TSG RAN WG1 Meeting #86bis
Lisbon, Portugal, October 10th – 14th, 2016
Agenda item 7.2.7

## Slide 2: Background
In RAN1#86, the following agreement is achieved:
  For TDD UL/DL configuration 1~5, down-select between the following options for HARQ transmission:
    Option1: Only support adaptive HARQ transmission, i.e., the retransmission of a PUSCH in UpPTS is scheduled by a UL grant with NDI not toggled
    Option2: Support both adaptive and non-adaptive HARQ transmission. For non-adaptive HARQ transmission, the PHICH is used, and the PHICH timing is designed based on the following principle:
      Principle: To keep the backward compatibility, the PHICH corresponding to PUSCH in UpPTS can only be added in DL subframes including legacy PHICH region
  FFS if non-adaptive HARQ transmission is supported for TDD UL/DL configurations 0 and 6
  For TDD UL/DL configuration 0, reuse the UL index field in UL grant to schedule PUSCH in UpPTS.

## Slide 3: Proposals
For TDD UL/DL configuration 1~5
  Support adaptive HARQ transmission, and specify the timing from PUSCH to its ACK/NACK feedback in UL grant according to the following table
  Support non-adaptive HARQ transmission
    FFS the timing from PUSCH to its ACK/NACK feedback in PHICH
  FFS the following alternatives for configuration of adaptive and non-adaptive HARQ transmission
    Alt1: Adaptive HARQ and non-adaptive HARQ are configured by RRC signaling
    Alt2: Support configure UE with both adaptive and non-adaptive HARQ transmission, and the adaptive HARQ timing can override non-adaptive HARQ timing
TDD UL/DL Config | UL subframe index n |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
1 |  | 4 | 4 | 6 |  |  | 4 | 4 | 6 | 
2 |  | 5 | 6 |  |  |  | 5 | 6 |  | 
3 |  | 6 | 6 | 6 | 6 |  |  |  |  | 
4 |  | 6 | 6 | 6 |  |  |  |  |  | 
5 |  | 6 | 6 |  |  |  |  |  |  | 

## Slide 4: Proposals
For TDD UL/DL configuration 0
  Support the following two alternatives for timing from UL grant to PUSCH, and allow the eNB to configure which alternative to use by RRC signalling
    Alt1: the UL grant only schedule the PUSCH in UpPTS, i.e., add an interpretation of UL index field with both bits set to 0 as follows
      When MSB and LSB are set to 0, UE shall upon detection of a PDCCH with DCI format 0 in subframe n intended for the UE, adjust the corresponding PUSCH transmission in subframe n+m, with m in the following table
    Alt2: Change the interpretation of UL index field
      1)MSB=1, LSB=0: UE shall upon detection of a PDCCH with DCI format 0 in subframe n intended for the UE, adjust the corresponding PUSCH transmission in subframe n+k, with k given in the following table.
      2)MSB=0, LSB=1: UE shall adjust the corresponding PUSCH transmission in subframe n+7
      3)MSB=1, LSB=1: UE shall adjust the corresponding PUSCH transmission in both subframes n+ k and n+7, with k in the following table
TDD UL/DL Config | DL subframe index n |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
0 | 6 | 5 |  |  |  | 6 | 5 |  |  | 
TDD UL/DL Config | DL subframe index n |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
0 | 4 | 5 |  |  |  | 4 | 5 |  |  | 

## Slide 5: Proposals
For TDD UL/DL configuration 6, support the following timing design from UL grant to PUSCH
  Introduce two bits for UL index field in DCI for UL grant
  The UL index is interpreted as
    When MSB=1 and LSB=0: UE shall upon detection of a PDCCH with DCI format 0 in subframe n intended for the UE, adjust the corresponding PUSCH transmission in subframe n+k, with the value of k in the following table
    When MSB=0 and LSB=1: UE shall adjust the corresponding PUSCH transmission in subframe n+6
    When MSB=1 and LSB=1: UE shall adjust the corresponding PUSCH transmission in both subframes n+k and n+6, with the value of k in the following table
TDD UL/DL Config | DL subframe index n |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
6 | 7 | 7 |  |  |  | 7 | 7 |  |  | 5

## Slide 6: Proposals
For TDD UL/DL configuration 0 and 6
  Support both adaptive and non-adaptive HARQ transmission, and specify the timing from PUSCH to its ACK/NACK feedback in PHICH or UL grant according to the following table
TDD UL/DL Config | subframe index n |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
0 |  | 5 | 4 | 7 | 6 |  | 5 | 4 | 7 | 6
6 |  | 4 | 4 | 6 | 6 |  | 4 | 4 | 7 |