## Slide 1: WF on CSI-RS pooling
Ericsson, Samsung, LG
3GPP TSG RAN1 #86bis R1-1610705
Lisbon, Portugal, Oct. 10 – 14, 2016
Agenda Item: 8.1.4.3

## Slide 2: Way forward
A CSI-RS resource set should be supported whereby CSI-RS resources within the set may be dynamically shared/shifted amongst users
CSI-RS resources are configured in 2 steps
  Step 1: Pre-configure a set of K CSI-RS resources for a group of users through RRC configuration
  Step 2: For a given user, dynamically indicate N out of K (where N >= 1) of the CSI-RS resources from the set to enable CSI measurement in a given time window
    Study the following alternatives
      Alt 1: Dynamic signaling through DCI
      Alt 2: Dynamic signaling through MAC CE
  The CSI-RS transmissions can be dynamically indicated as one shot or multi-shot within the window