## Slide 1
3GPP TSG RAN WG1 Meeting #86bis R1-1610978
Lisbon, Portugal, 11st - 14th Oct 2016
Agenda item: 8.1.5.2
WF on NR RACH Procedure
Huawei, HiSilicon, NTT Docomo, Qualcomm, ETRI,
Intel, Nokia

## Slide 2: Background
The following agreements have been reached at RAN1#86:
  RACH procedure including RACH preamble (Msg.1), random access response (Msg.2), message 3, and message 4 is at least assumed for NR from RAN1 perspective
  Simplified RACH procedure, e.g., Msg.1 (UL) and Msg.2 (DL), should be further studied
    Details on Msg.1 and Msg.2 are FFS
    Study should include comparison with the above procedure (first bullet)
  The design of the random access procedure should take into account the possible use of single-beam and multiple-beam operations, including
    Non Rx/Tx reciprocity at BS or UE
    Full or partial Rx/Tx reciprocity at BS or UE
  In case that multiple beam-forming is applied to DL broadcast channels/signals for initial access
    RACH resource is obtained by UE from detected DL broadcast channels/signals
      FFS: Details on association
    Other mechanism w/o association is also considered
  Multiple occasions for RACH preamble transmission in a given time interval are considered
    Details are FFS
    Other mechanism is not precluded
  Study further RACH reception/RAR transmission in TRPs/beams other than the one transmitting synchronization signals

## Slide 3: Proposal
RAN1 is studying and some companies see potential benefits of a simplified RACH procedure consisting of two main steps (Msg1 and Msg2) for UEs.
RAN1 has discussed the following:
  The use of a UE identity in Msg 1
  Msg 2: RA response that is addressed to the UE identity in Msg 1
  FFS on the definition and choice of the UE identity
RAN1 to send LS to RAN2
RAN1 is aware that RAN2 is also studying the RACH procedure and RAN1 would like to inform RAN2 to take the above into considerations and would like to request any feedback if there is any concern on the simplified RACH procedure.