## Slide 1: WF on SRS-based UL link adaptation
LG Electronics, CATT, Huawei, HiSilicon, Samsung
R1-1610983
3GPP TSG RAN1 #86bis
Lisbon, Portugal, Oct. 10 – 14, 2016
Agenda Item: 8.1.4.2.

## Slide 2: Proposals
Precoded/non-precoded SRS based UL link adaptation procedures should be supported in NR, with at least following different procedures:
  UL data scheduling (MCS/precoder/rank) is based on non-precoded SRS transmission by UE
    Configurable number of SRS ports are 2, 4, or [8]. Other possible numbers FFS.
    FFS on precoder/codebook
  UL data scheduling (MCS/precoder/rank) is based on precoded SRS(s) transmission by UE
    Configurable number of SRS ports are 1, 2, or 4. Other possible numbers FFS.
    Multiple precoded SRS resources (if supported) can be configured.
    Precoder for SRS can be determined by UE based on measurement on DL RS if possible to take the advantage of reciprocity
    FFS on precoder/codebook
  UL data scheduling (MCS/precoder/rank) is based on a combination of non-precoded and precoded SRS transmission by UE.