## Slide 1: Way Forward on bandwidth adaptation in NR
MediaTek, Acer, CHTTL, III, Panasonic, Ericsson, Nokia, ASB, Samsung, LG, Intel…
R1-1611041
3GPP TSG-RAN WG1 #86bis
Lisbon, Portugal, 10th – 14th October 2016
Agenda item 8.1.2.2

## Slide 2: Motivation (1)
In NR, up to hundreds or thousands of MHz system bandwidth may need to be supported
In LTE, UE consumes over 60% power for low-data-rate services and PDCCH-only decoding and UE power consumption is scaled with its operating bandwidth
It’s more power efficient if a UE can adapt its operating bandwidth based on the incoming traffic

## Slide 3: Motivation (2)
UE bandwidth before ADC

## Slide 4: Proposals
At least for single carrier operation, NR should allow a UE to operate in a way where it receives at least downlink control information in a first RF bandwidth and where the UE is not expected to receive in a second RF bandwidth that is larger than the first RF bandwidth within less than X µs (FFS: value of X)
  FFS the first RF bandwidth is within the second RF bandwidth
    FFS the first RF bandwidth is at the center of the second RF bandwidth
  FFS the maximal ratio of the first RF bandwidth over the second RF bandwidth
  FFS detailed mechanism
FFS RF bandwidth adaptation for RRM measurement