## Slide 1: Physical Layer Considerations for Random Access Procedure in Massive MIMO NR
National Instruments
3GPP TSG RAN WG1 Meeting #87 R1-1612609
Reno, Nevada14th – 18th November 2016
Agenda item: 7.1.2.4
Source: National Instruments
Title: Physical Layer Considerations for Random Access Procedure in Massive MIMO NR
Document for: Discussion and Decision

## Slide 2: Forward Compatibility Problems with Current Access Procedure
Current LTE Protocol requires up to four of 14 symbols or time-frequencies resources per subframe to be allocated to Physical Downlink Control Channel (PDCCH).
Massive MIMO has already been demonstrated in experimental systems to support up to 20 channels of MU-MIMO. [1].
Channel Reciprocity based MIMO for above and below 6 GHz was discussed in RAN1#86 in following Way Forwards [2], [3], [4].
It is expected in the future for the amount of control resources required to support Massive MIMO to overwhelm any common control mechanism.
In order to ensure that in the NR spec, Massive MU-MIMO is fully enabled, a Multi-User PDCCH (MU-PDCCH) is needed.
Additionally, a random access procedure is desirable which supports channel reciprocity-based in order to support reciprocity beamforming especially for multi-antenna UE’s.

## Slide 3: Onboarding Users
In a Massive MU-MIMO system, one of the challenges in onboarding all of the users
One requirement of the initial access procedure is that it be capable of efficiently accomplishing this task
The use of reciprocity-based initial access is central to the onboarding of massive numbers of simultaneous users, as explained in this contribution.

## Slide 4: Options for RACH Preamble
For Massive MIMO the SRS must be configured for each UE. For higher UE antenna counts, knowledge of the number of antennas is required at the gNB in order to set up a reciprocity channel. In order to reduce latency and increase control channel spectral efficiency, it is recommended to communicate the number of antennas in the RACH Preamble, although it not necessary.
RACH Preamble w/o #Antennas
RACH Response
UE Capabilities
PDCCH Message
SRS
MU-PDCCH Message
RACH Preamble w/ #Antennas
RACH Response
SRS
MU-PDCCH Message

## Slide 5: New Channels and Capabilities for Massive MU-MIMO
In order to support the full capabilities of Massive MU-MIMO, the following additional channels, signals and/or capabilities are required.
  Reciprocity-based Random Access
  Light PDCCH and Light PDSCH
    For system information and random access responses
    Can be potentially combined into one channel
  Reciprocity Reference Signals
  MU-PDCCH

## Slide 6: Scaling of MU-MIMO
PSS
SSS
Light-PDCCH and Light PDSCH
MU-PDCCH
Random Access Preamble
Reciprocity Reference Signals
MU-PDSCH
MU-PUSCH
MU-PUCCH
MIMO Layers Required
PBCH

## Slide 7: PDCCH and PDSCH
Some basic messaging such as System Information (SI) and Random Access Responses (RAR) are required. Today, they are sent on PDCCH and PUSCH, could potentially be combined onto one channel. Regardless, in order to support Massive MU-MIMO, common control should be minimized.
Proposal 1: Support light PDCCH and light PDSCH in New Radio for Massive MU-MIMO.

## Slide 8: Random Access Signals
Random Access Preamble
  Up to eight antenna ports to be supported per UE.
  Root Chu, CS Chu and FD-Interleaving all considered for MUXing
  #Antennas communicated in RACH Preamble
  Wideband RACH considered for reciprocity
Proposal 2: Support enhancements to Random Access Preamble as specified above

## Slide 9: Reciprocity Reference Signals, MU-PUSCH and MU-PDCCH
Reciprocity reference signals to be transmitted by UE
Sets up MU-PUSCH transmission with all of the associated start-up signaling
This enables reciprocity-based MU-PDCCH
Proposal 3: Support Reciprocity Reference Signals to enable MU-PDCCH and MU-PUSCH in New Radio for Massive MIMO.

## Slide 10: Proposals
Proposal 1: Support light PDCCH and light PDSCH in New Radio for Massive MU-MIMO.
Proposal 2: Support enhancements to Random Access Signals as specified above
Proposal 3: Support Reciprocity Reference Signals to enable MU-PDCCH and MU-PUSCH in New Radio for Massive MIMO.

## Slide 11: References
[1] P. Harris et.al, “Serving 22 Users in Real-Time with a 128-Antenna Massive MIMO Testbed”, To be presented at IEEE International Workshop on Signal Processing Systems (SIPS 2016), Dallas.
[2] R1-168254, WF on UL MIMO transmission, Huawei, HiSilicon, China Unicom, Samsung, NTT DOCOMO, RAN1#86.
[3] R1-168179 WF on CSI measurement and reporting in NR, Huawei, HiSilicon, Ericsson, China Telecom, RAN1#86.
[4] R1-168388 WF on beam management, CATT, Samsung, National Instruments, ZTE, RAN1#86.
[5] R2-167850 Considerations on the Random Access Procedure in Massive MIMO NR, National Instruments, RAN2#96