## Slide 1: WF on Basics of LDPC Design
Ericsson, NTU, Qualcomm, Intel, Nokia, ASB, LG, Samsung
R1-1613093
3GPP TSG RAN WG1 Meeting #87
Reno, USA 14th - 18th November 2016
Agenda item 7.1.5.1

## Slide 2: Background
Agreement in RAN1#85
  The Parity check matrix of Quasi-cyclic like LDPC Codes is defined at least by a matrix H of size (mb×z)×(nb×z), which consists of sub-block matrices of size z×z, where each sub-block matrix is composed by circularly shifted matrices or zero matrices.

## Slide 3: Proposal 1
Code extension of a parity-check matrix is used for IR HARQ/rate-matching support
    Use lower-triangular extension, which includes diagonal-extension as a special case

## Slide 4: Proposal 2
For the QC-LDPC design, the non-zero sub-blocks have circulant weight =1
    Circulant weight is the number of superimposed circularly shifted ZZ identity matrices

## Slide 5: Proposal 3
In parity check matrix design, the highest code rate (Rmax,j ) to design j-th H matrix for is
  Rmax,j <=8/9
  Rmax,j is the code rate of the j-th H matrix before code extension is applied (0 j< J)
  Rmax,j is the code rate after accounting for the built-in puncturing, if this is applied in H matrix design
  Rate matching to support transmission code rate higher than Rmax,j is not precluded