## Slide 1: WF on Channel Coding Chain for eMBB Data
Ericsson, Qualcomm, Samsung, Intel
R1-1613097
3GPP TSG RAN WG1 Meeting #87
Reno, USA 14th - 18th November 2016
Agenda item 7.1.5.1

## Slide 2: Background
Agreement in RAN1#86bis
  The channel coding scheme for eMBB data is LDPC, at least for information block size > X
  FFS until RAN1#87 one of Polar, LDPC, Turbo is supported for information block size of eMBB data <= X
    The selection will focus on all categories of observation, including overall implementation complexity, regardless of the number of coding schemes in the resulting solution (except if other factors are generally roughly equal)
  The value of X is FFS until RAN1#87, 128 <= X <= 1024 bits, taking complexity into account
  The channel coding scheme(s) for URLLC, mMTC and control channels are FFS

## Slide 3: Proposal: Observation on Coding Chain
If a single-code solution is adopted for eMBB data, only a single coding chain is necessary for both specification, implementation, and testing
  The coding chain includes: MCS table, TBS table, code block segmentation, rate matching algorithm, HARQ scheme for IR and Chase combining, link adaptation, scheduler, DCI signaling, soft buffer management, memory management, latency management, …
If a two-code solution is adopted for eMBB data, two coding chains are necessary for both specification, implementation, and testing
  For turbo codes, the LTE coding chain can be largely reused in specification
Single-code solution has an advantage over two-code solution from this perspective