## Slide 1: WF on comb hopping for uplink DMRS
Intel, Qualcomm
3GPP TSG-RAN WG1 #87 R1-1613107 Reno, USA, 14th – 18th November, 2016
Agenda Item: 6.2.2.4.3

## Slide 2: Background
In RAN1 #86b meeting, it is agreed that companies are encouraged to bring system level simulations to RAN1#87 to show the gain of comb hopping.

## Slide 3: Observation
With comb hopping, up to 2.5 dB average SINR gain can be observed compared to the case without comb hopping and for some particular UEs the instant SINR gain can be up to 5dB.
Significant gain, i.e. up to 22% for cell edge throughput and up to 14% for cell mean throughput, can be observed in UMa with16Rx@eNB and high loading scenarios. The gain in UMi is reduced, but there are still 6% cell edge throughput gain and 3.3% cell mean throughput gain observed for 50% loading case. Therefore, comb hopping not only improves channel estimation accuracy in frequency selective fading channel, but also randomizes inter-cell interference.

## Slide 4: Proposal
Inter-slot and inter-subframe comb hopping is supported.
  Inter-slot comb hopping is dynamically indicated by the CS/OCC table in UL DCI
    FFS details of hopping pattern indication
  Inter-subframe comb hopping can be semi-statically configured by RRC signaling
  Both inter-slot and inter-subframe comb hopping can be enabled simultaneously