## Slide 1: WF on PSSCH DMRS randomization
CATT, LGE
3GPP TSG RAN WG1 Meeting #87 R1-1613112
Reno, USA 14th - 18th December 2016
Agenda item – 6.1.8

## Slide 2: Background
Agreements:
  DMRS randomization of a PSSCH follows the CRC of the SA in the same subframe as the PSSCH
  Discuss in RAN1#87 whether additional mechanism is needed for PSSCH DM RS randomization focusing on the single-subframe transmission case.

## Slide 3: Proposals
For the single-subframe transmission, the following Tx UE behavior shall be explicitly specified:
  Value of frequency resource location field is randomly selected among all the possible code points corresponding to the same subchannel number chosen by the Tx UE.
  Value of retransmission index field is randomly selected between 0 and 1.

## Slide 4: Example