## Slide 1: WF on search space design for multicast in FeMTC
Ericsson, Nokia, ASB, ZTE,Intel, …
R1-1613129
3GPP TSG RAN WG1 Meeting #87
Reno, USA, November 14-18, 2016
Agenda item 6.2.8.2

## Slide 2: Background
In RAN1#86bis meeting, regarding FeMTC Multicast, the followings are agreed:
Max channel bandwidth and max TBS for SC-MTCH PDSCH transmission to BL/CE UEs:
  Option 1: According to Rel-13 Cat-M1 limitations (i.e. 6 PRBs and 1000 bits)
  Option 2: Configurable per SC-MTCH (with minimum maximum values of 6 PRBs and 1000 bits)
Max channel bandwidth and max TBS for SC-MCCH PDSCH transmission to BL/CE UEs:
  Option A: According to Rel-13 Cat-M1 limitations (i.e. 6 PRBs and 1000 bits)
  Option B: Configurable per SC-MCCH (with minimum maximum values of 6 PRBs and 1000 bits)
From physical layer point of view,
  All four options are feasible.
  Option 2 may have performance benefits over Option 1.
The maximum number of on-going SC-MTCHs supported by SC-MCCH is reduced compared to LTE.
Send LS to RAN2 to
  Inform RAN2 that RAN1 assumes the maximum number of on-going SC-MTCHs supported by SC-MCCH is reduced compared to LTE
  Request RAN2 to inform RAN1 of the maximum number of on-going SC-MTCHs supported by SC-MCCH in FeMTC.
  Request RAN2 to inform RAN1 whether and how segmentation of SC-MCCH will be supported in Rel-14.
For the search space scheduling SC-MCCH
  UE monitoring of blind decoding candidates is based on FFS: Type1-CSS or Type2-CSS for MPDCCH
  Rmax, and G values are configured per SC-MCCH by higher layers
    FFS the configuration of other parameters, e.g., narrowband.
Frequency hopping is supported in multicast to BL/CE UEs at least for max PDSCH channel bandwidth of 6 PRBs.
  FFS whether the frequency hopping is controlled by the same SIB parameters as other DL transmissions or by separate SIB parameters and/or DCI

## Slide 3: Background
In RAN2#95bis meeting, regarding Multicast, the followings are agreed:
  We consider to make the following agreement (working assumption for now):
    MT (paging) vs. SC-PTM: MT (Paging) has higher priority than SC-PTM
    MO (except signalling) vs SC-PTM: UE implementation
    MO signalling vs SC-PTM: MO signalling has priority.

## Slide 4: Proposal
MPDCCH search space configuration (including narrowband, Rmax, G) for SC-MCCH is signalled in SIB20.
MPDCCH search space configuration (including narrowband, Rmax, G) for SC-MTCH is signalled in SC-MCCH.
For the MPDCCH search space scheduling SC-MCCH,
    UE monitoring of blind decoding candidates is reused from Type1-CSS.
    MPDCCH search spaces for SC-MCCH support fixed AL = 24 for a 2+4 MPDCCH PRB-set with distributed allocation.
MPDCCH search space for SC-MTCH is based on one of the following:
    Option 1: Type1-CSS
    Option 2: Type2-CSS