## Slide 1: WF on Spectrum Partitioning with Mixed Numerology
3GPP TSG RAN WG1 Meeting #87
Reno, USA 14th –18th November 2016
Agenda: 7.1.1
R1-1613158
AT&T, Ericsson

## Slide 2: Agreement from RAN1#86
Agreement:
At least up to 40 GHz for eMBB and URLLC services, NR supports CP-OFDM based waveform with Y greater than that of LTE (assuming Y=90% for LTE) for DL and UL, possibly with additional low PAPR/CM technique(s) (e.g., DFT-S-OFDM, etc.)
  Y (%) = transmission bandwidth configuration / channel bandwidth * 100%
  RAN1 specification will support transmission bandwidth configuration corresponding to Y up to approximately100%
  Some evaluations in RAN1 show that Y for a NR carrier can be up to 98% of the evaluated channel bandwidths for both DL and UL without complexity and latency constraints [R1-166093]
  Note: additional pre-processing techniques on top of CP-OFDM are not precluded, e.g., OTFS
Additional waveforms may be supported by NR for e.g. other services (e.g. mMTC)
It is recommended that RAN4 should target to support eNB/UE with Y significantly higher than 90% when defining the RAN4 requirements where the specification of Y should consider complexity and latency constraints
In-band frequency multiplexing of different numerologies is supported in NR for both DL and UL, at least from the network perspective
  It is expected that spectrum confinement on sub-band basis is specified as requirements on
    Transmitter side in-band emission and EVM requirements
    Reception performance in presence of other-subband interferer
    The definition of sub-band is FFS
From RAN1 perspective, spectral confinement technique(s) (e.g. filtering, windowing, etc.) for a waveform at the transmitter is transparent to the receiver

## Slide 3: Observations
In our view support of dynamic mix of different numerologies using both FDM and TDM is very important for NR [R1-1612363]
Still these aspects are not clear
  Scheduling of the UE in DL and UL
    Can we schedule the UE belonging to different numerologies in any part of the in-band spectrum for both DL and UL
  Configuration of the network and the UE with mixed numerology for data channels ?
    Can the network support mixed numerologies dynamically ?
    Can the UE support mixed numerologies dynamically ?

## Slide 4: Observations
Use Cases of Mixed Numerology
  eMBB
  URLLC
  Broadcast channels
  Integrated access and backhaul
  High Doppler UEs
When ever two or more of these use cases are supported on the same channel the need to support mixed numerology operation arises.

## Slide 5: Explanation
Scheduling
  Network can dynamically schedule UEs belonging to different Numerologies in any part of the system bandwidth in DL direction
    I.e. a UE with a given numerology in the DL is NOT restricted to only a portion of the system bandwidth
  Network can dynamically schedule UEs belonging to different Numerologies in ay part of the system bandwidth in UL direction
    I.e. a UE with a given numerology in the UL is NOT restricted to only a portion of the system bandwidth

## Slide 6: Explanation
Configuration of the Network and the UE
  The network is allowed to support mixed numerologies for data channels dynamically as described in Proposal 1
  The UE can be allowed to support different numerology for data channels semi-statically

## Slide 7: Proposal
UEs can be at least semi-statically configured to transmit and/or receive data with different numerologies within a cell
  FFS: if the numerology, from a UE point-of-view can be dynamically varied
The network can simultaneously configure different UEs within a cell with different numerologies
UEs configured with different numerologies may not be restricted to be scheduled in different non-overlapping parts of a carrier
  Implying that, from a network point of view, the numerology of a certain frequency-part of a carrier can be dynamically varied
  Does not mean that different UEs with different numerologies may be simultaneously scheduled in overlapping parts of a carrier
  FFS: If spectrum confinement (filtering, windowing, …) can be dynamically varied or not