## Slide 1
Way Forward – Multiplexing URLLC and eMBB
ZTE, ZTE Microelectronics, Qualcomm, Ericsson, Nokia, Samsung, Sharp
R1-1613161
3GPP TSG RAN WG1 #87
Reno, USA, 14th – 18th November 2016
Agenda item 7.1.1

## Slide 2
Background
Outcome from RAN#86b

## Slide 3
Background
Assumption of sporadic URLLC traffic
Dynamic resource sharing between URLLC and eMBB
  Could be supported by puncturing eMBB resources and transmit URLLC

## Slide 4
Background - Puncturing
Concept
  eMBB transmission is configured for all the available resources
  When URLLC traffic occurs, it gets higher priority and corresponding eMBB symbols are punctured
  The eMBB and URLLC resources can use the same or different SCS

## Slide 5
Background
Puncturing with symbol alignment
1ms
7 symb@15 kHz SCS
7 symb@15 kHz SCS
2symb MS @30kHz
eMBB, 15 kHZ SCS
4symb MS @30kHz
4symb MS @60kHz
2*4symb MS @60kHz
Mini-slots (MS) can be supported with different SCS and nr of symbols (e.g. 2 and 4)
Mini-slots aligned with symbols of eMBB baseline numerology allow for efficient puncturing
2 symb MS@15 kHz

## Slide 6: Proposal
Dynamic resource sharing between URLLC and eMBB is supported by
  Puncturing eMBB symbols
  URLLC transmission bursts align with symbol boundaries of eMBB numerology

## Slide 7: References
  [1] R1-1611288 URLLC/eMBB multiplexing, ZTE, Reno, Nov 2016
  [2] R1-1612287 About introduction of addition CP overhead, Reno, Nov 2016
  [3] R1-1612014 Mini-slot design for URLLC, Qualcomm, Reno Nov 2016

## Slide 8
Appendix
Puncturing – Support of extended CP
In the same way that mini-slots from the NCP famliy are symbol level aligned with the eMBB baseline numerology, also mini-slots/slots from other CP families shall be aligned with the eMBB baseline numerology, e.g. 49-CP [3]
UE’s with different radio channels can be multiplexed with the same baseline eMBB numerology
7-ECP
4NCP
4NCP
1ms
eMBB@15kHz
1 slot (E)CP
2*4OS MS
URLLC U1@60kHz
URLLC U2@60kHz