## Slide 1: WF on CDM Aggregation for NP CSI-RS
Samsung, LGE, Ericsson
3GPP TSG RAN WG1 Meeting #87
Reno, U.S.A, 14th – 18th November 2016
Agenda item: 6.2.2.3
R1-1613229

## Slide 2: Background
Agreements at RAN1#86bis
  FFS on additional CDM-4 pattern(s) at least for 28- and 32-port to support full power utilization within a single PRB.
  CDM-8 design for {24, 32} ports:
    At least for 32-port CSI-RS, at least one CDM-8 pattern exists which uses REs from more than 2 OFDM symbols
    FFS until RAN1#87:
      which CDM-8 patterns are useful, and
      downselection between:
        Alt 1: CDM-8 patterns are configured by aggregation of CDM-2/4 patterns
        Alt 2: CDM-8 patterns are defined in the specifications without explicit aggregation
    Overhead reduction for CDM-8 is FFS
    Note: CDM-8 can be supported in both normal and special subframes

## Slide 3: Proposals
CDM-8 patterns for {24, 32} ports can be configured by aggregation of CDM-2/4 patterns from different CSI-RS configurations
  RRC signaling details are FFS
  Possible combinations for 24 ports are FFS
    At least one of following options will be down-selected or merged in RAN1#88
      Example 1: Use CDM-4 based aggregation for 24 port CSI-RS, all CSI-RS configurations are on the same OFDM symbols
      Example 2: Use CDM-4 based aggregation for 24 port CSI-RS without any restrictions
      Example 3: Use CDM-4 based aggregation for 24 port CSI-RS, where REs in the resulting CDM-8 groups are separated by a maximum of 6 OFDM symbols
  Possible combinations for 32 ports are FFS
    At least one of following options will be down-selected or merged in RAN1#88
      Example 1: Use CDM-2 based aggregation for 32 port CSI-RS without any restrictions
      Example 2: Use CDM-2/-4 based aggregation for 32 port CSI-RS without any restrictions
      Example 3: Use CDM-2/4 based aggregation for 32 port CSI-RS, where REs in the resulting CDM-8 groups are separated by a maximum of 6 OFDM symbols
  A CDM-8 pattern comprises CSI-RS configurations with same comb-offset, if configured